UNITED NATIONS DEVELOPMENT PROGRAMME

INTER-AMERICAN DEVELOPMENT BANK

Government of Brazil

BRA/09/G31 - Market Transformation for Energy Efficiency in Brazil

PIMS 3665, GEFSEC Project ID: 2941

Summary: The broad development goal of the project is to influence, transform and develop the market for energy-efficient building operations in Brazil and move towards a less carbon-intensive and more sustainable energy consumption path in the country. The project will contribute to improve energy efficiency in the commercial and public buildings sectors by 4.00 million MWh of electricity over 20 years, and directly reduce greenhouse gas emissions by 2.01 million ton CO2 equivalent over the same period with estimated post-project and indirect emission reduction of 16.06 tCO2. It will reinforce the local economy by decreasing the dependency of the country on imported fossil fuel and reducing building operation costs for project owners/operators. The project promotes cross-convention synergy by reducing GHG and CFC emissions through improving energy efficiency in buildings.

Acronyms

ABESCO	— Associação Brasileira das Empresas de Serviços de Conservacao de Energia

ABESCO	— Associação Brasileira das Empresas de Serviços de Conservacao de Energia

ANEEL 	— Agencia Nacional de Energia Eletrica

APR 		— Annual Project Report

AWP		— Annual Work Plan

BNDES	— Brazil National Development Bank

CC		— Climate Change

CFC		— Chlorofluorocarbons

CO		— Country Office

CO2		—  Carbon dioxide

CONPET	—  Programa Nacional Da Racionalização Do Uso Dos Derivados Do Petroleo E Do Gas Natural

CTA		—  Chief Technical Advisor

EE 		— Energy Efficiency

EDIFICA	— Programa de Eficiência Energética em Edificações

EEGM		— Energy Efficiency Guarantee Mechanism

ESCO		— Energy Service Company

EPC		— Energy Performance Contracting

FEBRABAN 	— Federacao Brasileira dos Bancos

GDP 		— Gross Domestic Product

GEF 		— Global Environment Facility

GHG		— Greenhouse Gas

GOB	— Government of Brazil

HVAC	— Heating, Ventilation, Air Conditioning

IDB	— Inter-American Development Bank

INMETRO 	— National Institute of Metrology, Normalization and Industrial Quality -

M&E	— Monitoring and Evaluation

MLF		— Multilateral Fund for Implementation of the Montreal Protocol

MMA		— Ministry of Environment

MME		— Ministry of Mines and Energy

MP		— Montreal Protocol

NPSC		— National Protect Steering Committee

PBE		— Brazilian Labeling Program

PBI		— Public Building Initiative

PGM		— Performance Guarantee Mechanism

EEGM		— Energy Efficiency Guarantee Mechanism

PIR 		— Project Implementation Review

PMU		— Project Management Unit

PROCEL	— Programa Nacional de Conservação de Energia Elétrica

PROESCO	— Programa Apoio a Projetos de Eficiência Energética

PROZON	— Inter-ministerial Executive Committee for the Montreal Protocol

RCU	— UNDP/GEF Regional Coordination Unit

SMEs 		— Small and Medium Enterprises

TOE 		— Tons of oil equivalent

UNDP	 	— United Nations Development Program

UNFCCC	— United Nations Framework Convention on Climate Change

USD	— United States Dollar

TABLE OF CONTENTS

SECTION A.	ELABORATION OF THE NARRATIVE	4

1.	Situation analysis	4

1.1	Context and global significance	4

1.2	Baseline and barrier analysis	5

1.3	Stakeholder analysis	8

2.	Project strategy	9

2.1	Institutional, sectoral and policy context	9

2.2	Project rationale	10

2.3	Policy conformity	12

2.4	Project Objectives, Outcomes and outputs /activities	12

2.5	Project Indicators, Risks and Assumptions	26

2.6	Incremental reasoning; expected global, national and local benefits	28

2.7	Country ownership: country eligibility and country drivenness	29

2.8	Sustainability and replicability	30

3.	Management Arrangements	31

4.	Monitoring and evaluation	32

5.	Legal context and other agreements	37

SECTION B.	STRATEGIC RESULTS FRAMEWORK; GEF INCREMENT	38

1.	Incremental cost analysis	38

2.	Strategic results framework (SRF)	42

SECTION C.	PROJECT BUDGET	47

SECTION D.	Additional information	49

1.	Co-financing letters and letters of endorsement	49

2.	Stakeholder involvement plan	50

3.	Operational rules of the EEGM	52

4.	EEGM guarantee exposure and investment leveraging	55

5.	Terms of reference of key project staff	57

- ELABORATION OF THE NARRATIVE

- Situation analysis

This chapter provides an overview of the significance of the “Market Transformation for Energy Efficiency in Buildings” project in the Brazilian and global context, which is followed by an analysis of the baseline situation and identification of key stakeholders.

  - Context and global significance

- In Brazil electricity supply is dominated by large hydroelectric plants. Hydropower provides more than 75% of Brazil's 90.7 GW of power generation capacity (excluding 12.6 GW of Itaipu). There is a relatively large use of biomass in industry and alcohol in transport, little use of coal outside the steel industry, and the use of natural gas is negligible. Total primary commercial energy use was 287 million tons of oil equivalent (TOE) in 2004. On the demand side, the overall energy intensity of Brazil's economy has increased 13% between 1980 and 2004 - especially for electricity. The electrical intensity of both the residential and commercial sectors has doubled since 1980, while the energy (electricity and fossil fuels) intensity of the industrial sector has remained fairly stable. Overall, Brazil is increasing its energy consumption per unit of gross domestic product (GDP). While greenhouse gas (GHG) emissions per unit of GDP are among the lowest in the world, they are increasing steadily. Moreover, environmental regulation imposes additional limits to accessing remaining potential additional hydro-electric generation sites.

- As a result of economic expansion, industrialization and growing urbanization during the 1970- 2000 period, Brazil’s power sector grew fast. Within overall energy supply, electricity went up from 19 to 41%, the use of firewood, charcoal and sugar-cane bagasse dropped significantly (from 40 to 20%), and oil by-products use declined from 38 to 32%. Presently, electric energy use is growing at a rate of 5.7 % (see table 1), per year.  Future electric energy demand is expected to be met through natural gas, coal, and hydro resources. To meet power demand, while simultaneously avoiding pollution-related impacts, the Government of Brazil is following a three-prong approach: a) introducing wide power sector reforms, including pricing and regulations, to enhance competition and private sector participation; b) encouraging energy efficiency (EE) and energy conservation measures; and, c) encouraging the demonstration and deployment of renewable energy technologies.

- In the medium and long term there are clear prospects of electric power consumption growth based on a) projected population growth (from 167 million inhabitants in the year 2000 to nearly 200 million inhabitants in 2015), and b) ongoing economic expansion.  The long-term forecast, (2000-2015), for the economy and the electric power market, suggest that electric power consumption will outpace growth in GDP as reflected in Table 1 below. Electric power consumption in Brazil will increase from 373 terawatt-hour (TWh) in the year 2005 to 617 TWh (base case) or 657 TWh (optimistic scenario) by the year 2015.

- The expected expansion in electric power consumption will require an increment in Brazil's installed capacity from 94 gigawatts (GW) in the year 2006 to approximately 135 in 2015. This corresponds to an addition of 41 GW generating capacity over the 2006/2015 period. Therefore, several different primary sources will have to be utilized for electric power generation. Brazil has an abundance of primary energy sources for electric power generation: hydroelectric potential, coal, uranium (nuclear power) and alternative sources (such as biomass, solar energy and wind energy). On the other hand, oil and natural gas reserves available in Brazil are not sufficient for a large-scale conventional thermoelectric generation expansion program.

Table 1: Energy consumption growth in Brazil - 2000/2015

| Average Annual Growth - (%) |
| --- |
|  | Base Case | Optimistic |
| Gross Domestic Product | 4.3 | 5.3 |
| Electric Power Consumption | 4.7 | 5.7 |

- Thus, unless the rate of investment in new generation capacity increases in the near future, and/or EE enhancement potential is actively tackled, serious energy shortages could be experienced post 2008, especially if projected economic growth targets are met. As a result, greater dependence on thermal options is expected to be the trend. The government of Brazil has been actively promoting EE activities through a variety of programs for the last two decades.  However, despite various initiatives and efforts to stimulate the market to improve EE (described below), there remain significant barriers to implementing such measures that involve both marketing to consumers and financing.

  - Baseline and barrier analysis

Baseline analysis

- Brazil has ratified both the Kyoto Protocol to the United Nations Framework Convention on Climate Change (UNFCCC), which addresses emissions of greenhouse gases, and the Montreal Protocol on Substances that Deplete the Ozone Layer. The objectives of the present project of market transformation for EE in buildings will contribute to meet Brazil’s commitments under both Protocols.

- Brazil has an enormous energy savings potential in all sectors of its economy. Energy saving policies and programs represent a potential least-cost contribution to the National energy supply in the medium and long term. Significant energy savings can be obtained through initiatives addressing heating, ventilation and air conditioning (HVAC) systems in private and public buildings. In commercial and public buildings, 64% of the energy consumption corresponds to air conditioning and lighting.). In the industrial sector, the total potential is of the order of 10-15 percent of total consumption per year.

- Based on a rough evaluation, it can be estimated that the Brazilian energy efficiency (EE) market in the building sector represents approximately USD 4.77 billion per year. But, the current market opportunities for EE projects are limited due to a lack of confidence by both the end-user and the lender in the guaranteed energy savings projections provided by Energy Services Companies (ESCOs). Local banks are not familiar with the performance risk associated with energy savings projects and are not willing to consider energy savings as collateral. Funding opportunities for EE projects remain limited as accessing third party financing and performance-based contracting, is virtually impossible for public buildings due to legal barriers, and lack of knowledge and understanding by various public sector stakeholders.

Barriers to Energy Efficiency in Brazil

- The major historical barriers to Brazilian energy efficiency investments have been an unstable economy and subsidized energy, particularly with respect to electricity prices.  In addition, very high import duties are applied on all imports, including EE equipment. The recent stabilization of the Brazilian economy and the movement of energy prices toward cost-based pricing, however, provide a growing incentive for EE investments.  In 2005, the power tariff was on average USD0.12/kWh for the public sector and USD0.14/kWh (including tax) for the commercial sector.

- The Brazilian EE services industry encounters many barriers involving both marketing to consumers and financing. These barriers include:

At the customer level:

- Poor understanding of potential benefits;

- Low priority of EE improvements;

- Perceived difficulties in financing in a high interest rate environment;

- Very few building owners/operators have implemented EE projects and they are reluctant to invest in projects with long payback periods

- Lack of confidence in the projected energy savings provided by ESCOs;

- Staff responsible for operations and maintenance feel threatened by the EE service provider;

- Tendency to treat an ESCO as just another consultant.

At sector level:

- In the private sector, lack of leadership to promote EE benefits;

- In the public sector, a difficult legal environment for tendering projects (accessing third party financing and performance-based contracts through, for example, ESCOs, is virtually impossible for public buildings due to legal barriers, and lack of knowledge and understanding by the various public sector stakeholders);

- EE techniques in the development and implementation of EE projects in buildings, particularly in the complex HVAC sector, remain poorly understood by building owners/operators/designers.

At EE services supply level:

- Limited utility involvement;

- High transaction costs in marketing to customers;

- Almost no commercial bank or third party equity financing available for EE projects to date; financial institutions (FIs) lack access to performance risk mitigation options which enhance their confidence in financing of EE initiatives.

- Mistrust toward commercial ESCOs, high interest rates, high collateral requirements.

ESCOs specific barriers

ESCOs in Brazil confront the following specific barriers:

- ESCOs function mostly on a fee for service basis. They have little retained earnings, virtually no capital, and limited capacity to borrow against their assets;

- They lack access to financing (as do many of their clients) without an adequate “balance 	sheet”;

- There is lack of  know-how among banks on lending to SMEs in general, and ESCOs in 	particular;

- Long-term revenues can be projected from their EE projects but banks do not see the contract cash flow as adequate collateral;

- Performance contracts are still little known by the market;

- Interest rates for local currency financing are significantly higher than for US Dollar financing, with average 12-15% p.a. for good corporate credits and up to 50% p.a. for smaller companies with weaker balance sheets. The average cost of capital is currently at 16% p.a.;

- Access to the public sector market is very limited and attempts remain largely unsuccessful because of the restrictive legislative and contractual environment. The major issue is the detailed technical description of project parameters required prior to tendering for services. To add to this impediment, the law stipulates that these parameters be developed by an entity that is legally distinct from bidding companies.

Financing energy efficiency initiatives:

- EE projects can be financed in different ways:

- Clients finance the projects directly through their own balance sheets;

- Guaranteed savings. Under this model the client obtains a loan, but the risk of technical performance is allocated to the ESCO. The value of energy savings should be sufficient for the client to service the debt and provide net financial benefits to both client and ESCO. If the savings goal is not met, the ESCO pays the shortfall;

- Shared savings. Under this model the ESCO finances the project, either with its own equity and/or through a loan from a bank. The ESCO will approach the end-user with a proposal to improve the energy efficiency of its building. After the assessment of existing conditions and the design of the EE project, a shared energy savings amount will be negotiated, which should amortize the total project costs (see below) through the resulting energy savings. The ESCO and its client sign an EE implementation contract (the “EE Contract”). The EE Contract will require the client to pay to the ESCO periodic amounts equal to a percentage of the savings realized in the client’s energy bill.

- Currently, the typical energy conservation project in Brazil has an estimated cost of USD 250,000 (not including financial cost) and potential savings of about USD 500,000. A typical EE project process includes evaluation (energy audit and feasibility study), project design, commissioning, implementation and measurement and verification of energy savings. The savings should cover the client’s share of savings, reimbursement of project investment cost contributed by the ESCO, the ESCO’s debt obligation and the ESCO’s profit margin. A calculation example is given in Table 5.

- ABESCO estimated two years ago that the volume of energy conservation projects undertaken annually represents only about USD25 million with the potential to reach ten times this number by the end of the decade. Of the above-mentioned barriers. The lack of access to specific project financing has been identified as the main barrier for the development of EE projects in Brazil, and for the development of a sustainable ESCO market in the country. Due to limited availability of credit EE projects are generally financed internally by the client or by the ESCOs themselves. Most projects are not carried out as performance contracts. High interest rates and difficulty in accessing adequate terms relative to the economic benefits of projects have also been limiting the interest and capacity of end users and ESCOs to use debt financing for the implementation of EE projects.

- Two programs have been designed to tackle some of these problems. The first is the “ANEEL Fund”, as it is referred to in Brazil. Under current regulation, the utilities must spent 1% of their annual net revenues on public-benefit investment in the energy sector, of which half on energy efficiency. Assuming a power market in Brazil of 387 TWh (2007) and an average power tariff of USD 0.10/kWh, the annual amount for EE investment through the ANEEL Fund is around USD 190 million. In practice, the Fund’s resources are used by the utilities within their own department or for of institutional clients who do not pay their electricity bills (public sector), thereby reducing the losses incurred by the utilities with these clients.  The Fund has become an important source of income for some ESCOs as utilities regularly outsource to ESCOs. However, it is important to note that the market is essentially dominated by around 10 firms, often subsidiaries of utilities that act as intermediaries in the development and the implementation of EE projects.  There is a very limited number of other facilitators in the market and the ANEEL model cannot be regarded as a commercial mechanism that can trigger the EE market by private sector actors.

- The second program is PROESCO, designed by BNDES (the Brazilian National Development Bank) with support of the World Bank, was launched at the beginning of 2008. Under PROESCO BNDES can lend directly if the loan is above BRL10 million and through commercial banks if the amount is less. Due to the low interest rate (TJLP) at which it funds participating banks, BNDES offers loans at rates (about 12% p.a. all-in) that are lower than commercial rates in BRL (about 16-30% p.a.). Under PROESCO, BNDES assumes up to 80% of the risk on loans that would be in default (including capitalized interest). The maximum loan period is 6 years with a grace period of 2 years. The borrower may be the client (end-user) or project developer (ESCO) and must present a request for financing to a participating financial institution. The PROESCO mechanism was aimed at addressing the lack of capacity among banks to lend to ESCOs, and at providing a solution to the high interest rates faced by end users and ESCOs for the implementation of EE projects. In this respect, PROESCO was well conceived. ESCOs and banks reacted very positively to PROESCO and during 2007 rapidly developed 27 projects to be presented to the new facility.

- Unfortunately, many barriers were faced by BNDES in the implementation of PROESCO such as: 1) the lack of capacity among local financial institutions to efficiently evaluate projects, 2) difficulty of banks to account for and accept partial credit cover and to rely on more than one source of collateral, and 3) the institutional incapacity of BNDES to deal with the projects presented to the program due to the lack of the necessary human resources.  These problems have prevented the EE project applications from being approved by BNDES and by the banks, with the result that ESCOs and banks stopped developing projects for presentation to PROESCO. The latest news heard from BNDES is that they have found a potential way to address some of these issues, such as relocating the program within a new operational division of BNDES’ environmental department, and possibilities remain that ESCOS could be able to benefit from PROESCO at last in a foreseeable future, even though this cannot be guaranteed at this time.

  - Stakeholder analysis

- During the preparatory (PDF B) phase consultative meetings with various stakeholders (see the list below) and key market players revealed that the private sector is willing to integrate EE considerations in the buildings operation process under specific conditions, including: (i) having the government take the leadership on this issue through retrofitting of its own buildings; and, (ii) having a specialized financial mechanism in place to help mobilize investment resources from within the banking system.

- The role of the government will therefore, be key to the participation of others stakeholders in this project. The Ministry of Environment (MMA - Ministério do Meio Ambiente) has been strongly supportive of this project from the beginning and will act as a Leading Executing Agency and will work in close cooperation with other relevant ministries.  The Ministries of Mines and Energy, Finance, and Public Planning, as well as the MMA will oversee the global implementation of the project during its entire execution as part of the national program steering committee together with national banks and various private sector representatives.

- Furthermore, as the project will need the support of a wide range of stakeholders within the market, it is expected that the project implementation will be coordinated in conjunction with the following stakeholders:

- Programa Nacional de Conservação de Energia Elétrica (PROCEL) will provide technical expertise to Ministry of Mines and Energy and will contribute in the CB program component implementation.

- Brazil National Development Bank (BNDES) is starting to implement the PROESCO EE financing facility. One product of the IDB/UNDP sponsored Energy Efficiency Guarantee Mechanism (EEGM) will offer co-financing guarantees to ESCOs to complement their access to debt financing through PROESCO;

- Agencia Nacional de Energia Eletrica (ANEEL), which requires utilities to use a percentage of their annual net revenues for EE and public benefit investments;

- The United States Agency for International Development (USAID), which is involved in public building EE strategy. The PBI component will take advantage of their evaluation of legal aspects for public buildings to access ESCOs technical and financial services.

- ESCOs, such as Light ESCO, Vitalux, Ecoluz, Ecoenergy Brazil, Efficientia, ESCO Electric and Pterobras Distribuidora S.A.

- Banks that are PROESCO partners, such as Banco Itau, Bradesco, Banco do Brasil, BDMG (Minas Gerais Development Bank) and CEF (Caixa Econômica Federal) as well as other banks that have shown interest in EE, such as Banco Real, Unibanco and financial institutions such as Rio Bravo Investimentos

- Associação Brasileira das Empresas de Serviços de Conservacao de Energia (ABESCO) will assist in promoting the various activities included in the Brazil Market Transformation for EE in Buildings program. ABESCO currently has about 70 members.

- Associação Brasileira de Refrigeraçáo, Ar Condicionado, Ventilaçáo e Aquecimento (ABRAVA) will assist ESCOs in their efforts to take advantage of the Project.

- Federacao Brasileira dos Bancos (FEBRABAN) will act as a potential trainee/ partner, and linkage to banks for financing of EE programs.

- Other stakeholders are also expected to collaborate in the project implementation, as it is more widely marketed and gains renown.

- Project strategy

  - Institutional, sectoral and policy context

The key institutional, sectoral and policy elements identified in the country are presented below:

- Law 9991 and ANEEL Law # 9991 dated 24 July 2000 mandates electricity distribution companies to spend a minimum of 1% of their operational liquid income in public-benefit investments and R&D, including 0.5 % in energy efficiency programs. This percentage may change in time; up to 31 December 2005, the percentage breakdown was 50-50.  Investments are to be applied according to the Agencia Nacional de Energia Eletrica, (ANEEL) regulations. ANEEL was created by Law 9427 (1996) to regulate and control the production, transmission, distribution and commercialization of electricity in Brazil.

- PROCEL (Programa Nacional de Conservação de Energia Elétrica) In order to reduce the growing demand and consequently reduce the need for new, costly supply side investments, the Government of Brazil has adopted policies and measures with stronger emphasis on energy efficiency. Under Eletrobrás responsibility, and with close links with MME, the PROCEL program (Programa Nacional de Conservação de Energia Elétrica) was created in 1985. Its objective is to promote the rational use of electricity by, among others, households, industry, water utilities and in public buildings and public lighting. The CONPET program, created in 1991, aims at encouraging the efficient use of petrol and natural gas derivates in transport, commerce, industry and agriculture.

- Promotion of energy efficiency (EE) standards and labeling. Under the framework of the Brazilian Labeling Program (PBE), established in 1983 and managed by the National Institute of Metrology, Normalization and Industrial Quality (INMETRO), Brazil applies a voluntary labeling scheme for energy consuming equipment. To accelerate market transformation for a specified list of equipment, starting on 2006 labeling is to become mandatory. International EE standards (IEC, ISO, and ASHRAE) have been adopted. In association with the PBE, PROCEL have developed marketing activities to assist private stakeholders to cope with this new regulation, for example an award for the most efficient electric projects in the market for each type of equipment. Parallel to PBE, Law 10.295 (of October 2001) states that minimum energy efficiency or highest energy consumption standards are to be established for energy consuming equipment and buildings in the future. This measure prevents manufacturers from shifting their production to undesired EE levels.

- Under PROCEL Management since 2003, the EDIFICA Program (Programa de Eficiência Energética em Edificações) is responsible to organize actions and set targets for improvement that would lead to the development of  (i) establish minimal requirements to integrate the architecture of the buildings to the environment and to the natural resources; (ii) create EE indicators for buildings; (iii) certificate material and equipment, establish procedures for regulation/legislation; (iv) create mechanisms to provide financial resources and the removal of barriers to the implementation of projects and (v) promote educational and of social interest projects.

- Energy Service Companies (ESCOs). ESCO experience in Brazil is recent and limited. Most EE service providers are small to medium sized engineering consulting firms and few make a living focused predominantly on energy efficiency (EE) services. Most successful ESCOs are linked to utilities that use partially their ANEEL funds in the market. ABESCO, the Association of Brazilian Energy Service Companies (ABESCO) was founded in 1997 by 15 members to represent and promote the ESCO industry in Brazil, but only but only began to take off in early 2001. Today, ABESCO has more than 72 members, 58 of which are ESCOs. ABESCO's mission includes the promotion of the energy efficiency industry in Brazil and the competitive improvement of Brazilian companies through the sustainable development.

  - Project rationale

GEF alternative scenario and project implementation strategy

- To help removing the above-mentioned finance, capacity, technology and policy barriers that currently stand in the way of the widespread adoption of energy-efficient measures and technologies in buildings in Brazil, GEF support is requested in the amount of USD 13.5 million to implement a capacity building and  financial tools and mechanisms program that will help realize market transformation. There is significant potential to achieve energy savings and reduce greenhouse gas emissions from the buildings market in Brazil, The program will encourage cross-convention synergies with the Montreal Protocol Chemicals to include a chiller replacement component, thus contributing to the phase-out of CFCs. The project will positively influence the EE market in Brazil and will help chart a less carbon-intensive and more sustainable energy consumption path in Brazil and subsequently in the Latin American Region as a whole.

- The project will strive to remove the identified barriers through a comprehensive and integrated approach that will focus on:

- Building awareness and capacity amongst various market actors;

- Creating a favorable policy and financing environment to eliminate the barriers specific to the implementation of EE projects in public buildings and facilities;

- Establishing an integrated approach for potential EE enhancement in buildings while demonstrating the EE potential of CFC-based chillers replacement; and,

- Under the lead of the IDB, implementing an energy efficiency financial facility to reduce the risks perceived with financing EE projects.

- To address capacity barriers with respect to a the institutional framework and the lack of awareness amongst target end users, this GEF intervention will support a nationwide technical assistance program targeted to all of the relevant stakeholders identified during the PDF-B phase. This program will develop a range of knowledge products focusing on the technical, environmental and economic merits, and technical options (associated with EE practices) for public and private building owners or operators that can lead to broader scale replication in Brazil.

- Based on consultation with the Brazilian banking community, it has become apparent that technical performance risk is the one aspect of ESCO financing that presents the greatest challenge to local lenders. Therefore, the project seeks to address and substantially mitigate the performance risk aspects of ESCO projects by including a financial facility, called Energy Efficiency Guarantee Mechanism (EEGM) that will be set-up as a cost-effective and market-oriented approach to supporting investments in EE technologies for buildings as well as large-scale EE projects’ in Brazil by offering a number of guarantee products.

- The EEGM  will seek to directly eliminate many of the real, and perceived, risks at the financing level, and will effectively reduce the perceived risks of building owners/operators and financial institutions who will be involved in the project. The project will also provide building owners with financial incentives for the EE enhancement of their buildings. The GEF resources will be used together with guarantee capacity from the Inter-American Development Bank (IDB) to stimulate sustainable EE market transformation. Furthermore, the EEGM is intended to complement PROESCO and not to compete with it.

- By taking a holistic view of the market, and by targeting both the supply and demand side of the EE technologies market, the project will boost its chances of success and hence increase its potential impact on reducing GHG emissions.  Improving EE in building operations will contribute to lowering GHG emissions from an energy consumption perspective, as well as through the reduction of CFC emissions which have a very high global warming potential. The implementation of this project will position Brazil as one of the front runners in the area of market transformation through uptake of EE technologies, with wide-ranging applications and replication potential outside Brazil.

- In the absence of the project’s interventions, Brazil’s EE efforts would likely remain in their current state or, given the reforms presently underway in the sector, funding for EE enhancement may start to decline as deregulation of the energy sector advances. Under the baseline scenario, demonstration of emerging technologies and market driven EE delivery mechanisms would be restricted. Investments in EE would most likely remain in Government hands, through the use of subsidized loans to state governments and qualifying enterprises. Information dissemination on EE financing and practices would remain hampered if no structured demonstration of best practices and monitoring of savings is achieved.  Institutional capacity to implement innovative EE measures would remain fragmented and, most likely, at a centralized level.  Participation of private investors and ESCOs would be delayed without the introduction of performance enhancement mechanisms to address performance risk in EE projects.

  - Policy conformity

- The proposed project conforms to GEF Operational Program 5: Removal of Barriers to Energy Efficiency and Energy Conservation by removing barriers to the large-scale application, implementation, and dissemination of cost-effective, energy-efficient technologies and practices that will result in the reduction of greenhouse gas emissions in Brazil. Within this Program, the project supports the (GEF-4) Strategic Objective CC1: Promoting energy-efficient buildings and appliances.

- The project seeks to improve the EE of buildings and appliances in Brazil by: (i) reinforcing the capacity of market actors in EE building activities; (ii) increasing market activities related to EE projects development and implementation in the buildings sector; (iii) designing an innovative energy efficiency guarantee mechanism (EEGM), (iv) increasing the number of EE appliances; and, (v) monitoring the results of project’s activities. The Government’s support for this EE Project is consistent with its strategy of improving efficiency of energy supply and use, and enhancing private sector participation. GEF support would help to develop ‘state of the art’ capacity in buildings EE, develop a mechanism for the implementation of EE projects in public sector buildings, implement an innovative financial mechanisms to create the conditions for the implementation of a sustainable buildings EE market, disseminate information on buildings EE potential and benefits and, create best practice information on the adoption of EE in the Brazilian markets

  - Project Objectives, Outcomes and outputs /activities

Project goal and objective

- The goal of the project is to influence, transform, and develop the market for energy-efficient building operations in Brazil and move towards a less carbon-intensive and more sustainable energy consumption path in the country. The project will contribute to improving EE in the Brazilian commercial and public building sectors by 4.00 million MWh of electricity over 20 years, and will contribute to direct project GHG emissions reductions in the order of 2.01 million tons of CO2 and additional direct post-project and indirect emission reduction of about 16.06 million tons of CO2.

- The objective of this project is to foster EE investments in private and public buildings, by addressing the technical and financial barriers (mentioned above in paragraph 1.3) which persist despite past and present public and private sector programs/initiatives in this domain.

Outcome 1	Enhanced EE investments through Capacity Building (CB) in private and public sector buildings

- The project will finance a capacity building component that will develop best practice capacity in Brazil in the identification, formulation, implementation and management of EE projects in the buildings sector. This capacity development exercise will be designed to reach a wide range of EE services providers (ESCOs and other energy service providers), as well as building owners and operators (See Section IV, Part IV for details of the capacity building program). The program will serve to underpin the aim of market transformation by raising the level of knowledge and understanding amongst stakeholders.

Outputs are:

- Local energy product/service providers capacity strengthened through targeted training events (as detailed below);

- EE market players have greater awareness of interest in implementing EE measures. Up to 5,000 persons trained in the design, installation, operation and maintenance of building energy efficiency equipment and systems;

Table 2	Budget of component 1

| Outcome 1 Capacity Building EE |  | Units | Cost/unit | GEF | Co-financing |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | In cash | In-kind |
| LT consultants (training) | 2000 | days | 170 | 340,000 |  |  |
| Training and consultancy |  |  |  |  |  |  |  |  |
| - supplies, rental equipment |  |  |  |  |  | 26,300 |  |  |
| - printing, 5000 trainees |  |  | 5000 | trainees | 10 | 50,000 |  |  |
| - int'l consultants |  |  | 75 | courses | 1750 | 131,250 |  |  |
| - nat. ST consultants |  |  | 250 | courses | 1000 | 250,000 |  |  |
| - contractual services |  |  | 250 | courses | 953.68 | 238,420 |  |  |
| Travel |  |  |  |  |  |  |  |  |
| - trainers, 25 courses in 10 cities |  |  | 250 | courses | 500 | 125,000 |  |  |
| - travel, int'l consultants |  |  | 75 | courses | 2000 | 150,000 |  |  |
| - DSA, trainees |  |  | 5000 | trainees | 100 |  |  | 500,000 |
| - LT consultants , 50 trips |  |  | 50 | trips | 500 | 25,000 |  |  |
| Equipment |  |  |  |  |  | 19,000 |  |  |
| Miscellaneous (unforeseen) |  |  |  |  |  | 13,200 |  |  |
|  | TOTAL |  |  |  | 1,368,170 | - | 500,000 |

Note:

Outcome 1 ‘Enhanced EE investments through Capacity Building in private and public sector buildings’ aims at developing best practice capacity in Brazil in the identification, formulation, implementation and management of EE projects in the buildings sector. Since this capacity building component is very large and comprehensive, targeting administrators/owner buildings (800),   technical staff of buildings (1,400), service providers (consultants and ESCOs) (1,800), architects and engineers (800), and banks and other financial institutions (400), for a total of 5,000 trainees from different areas in Brazil. The training should be distributed around the country in at least 2 cities of each geographical region, i.e. the 8 biggest cities in Brazil plus the biggest cities of north and Middle East regions Therefore it has been estimated that the coordination needs of the technical content of the trainings as well as the logistics requires longer-term consultants.

- The training plan is proposed to be as follows:

- For administrators/building owners:

| Course | Place | Duration | # of trainees |
| --- | --- | --- | --- |
| Energy Management of Buildings | 10 cities | 1 day – 8 hours | 10 x 20 |
| Understanding Performance Contract and how to get bank financing | 10 cities | 1 day – 8 hours | 10 x 20 |
| Energy Efficiency in Buildings - Overview | 10 cities | 1 day – 8 hours | 10 x 20 |
| Monitoring the Performance Contract | 10 cities | 1 day – 8 hours | 10 x 20 |
| TOTAL | 800 |

- For technical staff of buildings:

| Course | Place | Duration | # of trainees |
| --- | --- | --- | --- |
| Energy Management of Buildings | 10 cities | 1 day – 8 hours | 10 x 20 |
| How to implement the Performance Contract | 10 cities | 2 days – 16 hours | 10 x 20 |
| Monitoring & verification - user's view | 10 cities | 1 day - 8 hours | 10 x 20 |
| EE technologies on buildings | 10 cities | 3 days – 24 hours | 10 x 20 |
| Air conditioning (AC) systems management | 10 cities | 1 day – 8 hours | 10 x 20 |
| AC systems maintenance and operation | 10 cities | 3 days – 24 hours | 10 x 20 |
| EE CFC-free chillers | 10 cities | 1 day – 8 hours | 10 x 20 |
| TOTAL | 1,400 |

- For service providers:

| Course | Place | Duration | # of trainees |
| --- | --- | --- | --- |
| Selling Performance Contracts | 10 cities | 1 day – 8 hours | 10 x 20 |
| Monitoring and verification | 10 cities | 2 days – 16 hours | 10 x 20 |
| Improving the identification and formulation of EE projects | 10 cities | 2 days – 16 hours | 10 x 20 |
| Improving the implementation and management of EE projects | 10 cities | 2 days – 16 hours | 10 x 20 |
| Financing EPC and EE projects | 10 cities | 2 days – 16 hours | 10 x 20 |
| Design of HVAC systems | 10 cities | 3 days - 24 hours | 10 x 20 |
| Operation and maintenance of HVAC systems | 10 cities | 3 days - 24 hours | 10 x 20 |
| EE and green technologies on buildings | 10 cities | 2 days - 16 hours | 10 x 20 |
| Analysis and evaluation of thermal EE project | 10 cities | 2 days - 16 hours | 10 x 20 |
| TOTAL |  |  | 1,800 |

- For banks and other financial institutions:

| Course | Place | Duration | # of trainees |
| --- | --- | --- | --- |
| Understanding EE market and projects | 4 cities | 1 day – 8 hours | 10 x 20 |
| Understanding ESCOs and Performance Contracts | 4 cities | 1 day – 8 hours | 10 x 20 |
| TOTAL |  |  | 400 |

- For architects and engineers to promote building regulations as requested by PROCEL:

| Course | Place | Duration | # of trainees |
| --- | --- | --- | --- |
| Energetic performance Simulation | 10 cities | 5 days – 40 hours | 10 x 20 |
| Applying the Regulation | 10 cities | 3 days – 24 hours | 10 x 20 |
| EE in building designs | 10 cities | 5 days – 40 hours | 10 x 20 |
| TOTAL |  |  | 600 |

Outcome 2	Access to EE services and commercial financing for public sector buildings enhanced with a Public Building Initiative (PBI)

- A Public Building Initiative program will be developed and implemented in order to eliminate the barriers specific to the implementation of EE projects in public buildings and facilities. The PBI has been designed to effectively tackle the current market barriers that are hindering the uptake of EE projects in the public building: a) lack of access to financial market and EE market players due to high credit risk; b)limited public investment budgets for upgrades of equipment/appliances and EE investments; c) lack of human resources trained to promote EE investment projects; d)lack of technical personnel with appropriate knowledge on how to implement EE projects; e) obstacles to existing legal and contractual frameworks where third party financing, either in the form of leasing or through a performance based contracting approach, are concerned.

- Therefore, from the operational perspective, the proposed PBI will be based on the promotion of Energy Performance Contracting (EPC) in the public sector in Brazil. The PBI will have the mandate to clear the way for federal, state and municipal public organizations/agencies to use EPC within their facilities, thereby encouraging introduction of adapted mechanisms to enable the use of such an approach in the public sector. The PBI will work at policy amendments that allow organizations to enter into energy performance contracts under their own authority in much the same manner as they currently pay their energy bills. To make the contracting process easier, the PBI will provide model contracting and assessment documents. These model documents will include requests for proposals, actual energy performance contracts, environmental assessments and other necessary policy and legal processes. The PBI will also provide a list of pre-screened private-sector firms qualified to bid for energy performance contracts. In addition, during the inception stage of the project an in-depth study is planned on the typical costs, electricity savings and payback periods for different types of buildings and regions in the country.

Outputs will include:

- Enabling institutional framework for EE project development in Public Sector is established; Revisions and amendments to the legal and contractual framework for the use of EPC in the public sector;

- EE Projects realized under the ESCO approach by the Government increased, (Public building owners/ operators have been exposed to PBI program to access EE services and applied its recommendations);

- Capacity Building offered to Public Building Owners/Operators and ESCOs in developing and implementing selected projects on a pilot basis for public sector buildings. A tailored executive and managerial support program established to encourage the use of the PBI.

Table 3	Budget, component 2

| Outcome 2 EE in public buildings |  | Units | Cost/unit | GEF | Co-financing |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | In cash | In-kind |
| LT consultants (training; policy) |  |  | 2000 | days | 170 | 340,000 |  |  |
| Training and consultancy |  |  |  |  |  |  |  |  |
| - supplies, rental equipment |  |  |  |  |  | 19,830 |  |  |
| - printing, 1600 trainees |  |  | 1600 | trainees | 10 | 16,000 |  |  |
| - int'l consultants |  |  | 24 | courses | 1750 | 42,000 |  |  |
| - nat ST consultants |  |  | 80 | courses | 1000 | 80,000 |  |  |
| - contractual services |  |  | 80 | courses | 1187.5 | 95,000 |  |  |
| Travel |  |  |  |  |  |  |  |  |
| - trainers, 8 courses in 10 cities |  |  | 80 | courses | 500 | 40,000 |  |  |
| - travel, int'l consultants |  |  | 24 | courses | 2000 | 48,000 |  |  |
| - DSA, trainees |  |  | 1600 | trainees | 100 |  |  | 160,000 |
| - LT consultants , 140 trips |  |  | 140 |  | 500 | 70,000 |  |  |
| TA and policy component |  |  |  |  |  |  |  |  |
| - int'l consultant |  |  | 155 | days | 700 | 108,500 |  |  |
| - nat. ST consultant |  |  | 600 | days | 400 | 240,000 |  |  |
| - travel |  |  |  |  |  | 39,000 |  |  |
| Publications |  |  | 7 | years | 3000 | 21,000 |  |  |
| Equipment |  |  |  |  |  | 9,000 |  |  |
| Miscellaneous (unforeseen) |  |  |  |  |  | 15,000 |  |  |
|  | TOTAL |  |  |  | 1,183,330 | - | 160,000 |

Note:

Outcome 2 ‘Access to EE services and commercial financing for public sector buildings enhanced with a Public Building Initiative’ focuses on the elimination of barriers specific to the implementation of EE projects in public buildings and facilities.

For this component long-term consultants are envisaged, first to concentrate on the coordination of the activities related to removing the existing legal and contractual frameworks obstacles where third party financing, either in the form of leasing or through a performance based contracting approach, is concerned, and, second, on the coordination of the training activities.  The capacity building program aims at training 1,600 people on 8 different topics, as detailed below.

- There are significant legal and regulatory barriers, such as Las 8666, that in practical terms inhibit performance contracting in the public sector in Brazil.   The PBI will focus on analysing existing laws and regulations and on proposing the most feasible modifications and lobbying to get these approved by the appropriate legislative bodies.

- The training plan is proposed to be as follows:

- For administrators and technical staff of buildings:

| Course | Place | Duration | # of trainees |
| --- | --- | --- | --- |
| Energy Management on Public Buildings | 10 cities | 1 day – 8 hours | 10 x 20 |
| Understanding Performance Contract | 10 cities | 1 day – 8 hours | 10 x 20 |
| Performance Contract Procurement | 10 cities | 2 days – 16 hours | 10 x 20 |
| Energy Efficiency in Public Buildings | 10 cities | 3 days – 24 hours | 10 x 20 |
| How to do a Performance Contract in public sector | 10 cities | 4 days – 32 hours | 10 x 20 |
| EE benefits and its impacts | 10 cities | 1 day – 8 hours | 10 x 20 |
|  |  |  | 1,200 |

| Course | Place | Duration | # of trainees |
| --- | --- | --- | --- |
| Performance Contract Procurement | 10 cities | 2 days – 16 hours | 10 x 20 |
| How to implement a Performance Contract in public sector | 10 cities | 2 days – 16 hours | 10 x 20 |
|  |  |  | 400 |

- For service providers (consultants and ESCOs):

Outcome 3: 	Interest enhanced in the replacement of energy-inefficient CFC-using chillers

- In support of the overall aim of enhancing national capacity for buildings energy efficiency, this project component will serve to stimulate interest in an integrated approach for potential EE enhancement in buildings by demonstrating the EE potential of CFC-based chillers replacement. While it is clear that individual chiller replacement based on EE considerations has not occurred due to of the long payback period, practical demonstration of the economic and environmental benefits of bundling EE initiatives in building systems is a logical and structured approach that is expected to be well received, by interested parties in the country.

- The key barriers to the accelerated adoption of new, energy efficient, CFC-free chillers and related system improvements are barriers that are largely shared by energy efficiency investments in the building sector in general. Integrating the two components under the larger project umbrella would serve to demonstrate synergies between environmental conventions that address seemingly disparate issues – climate change and ozone depletion.

- This project component will be funded using co-financing secured through the Multilateral Fund of the Montreal Protocol and from national stakeholders.

Outputs will include:

- Technical Assistance provided to professionals on EE improvement combined with HVAC equipment replacement. Improved capacities of at least 120 professionals (design engineers, ESCOs, building owners/operators, entrepreneurs, etc.) in CFC-based chiller replacement.

- Capacity building courses and practical on-the job exercises will be provided to professionals to increase their capacities;

- Technical guides drafted for professionals;

- Implementation of 40 pilot projects to evaluate the impact of the proposed CFC-based chillers replacement program.

Table 4		Budget, Component 3

Outcome 4: 	Energy Efficiency Guarantee Mechanism (EEGM) made available to stimulate EE investment through ESCOs

Typical EE cash flows and risk allocation

- Shared savings EE contracts are performance based contracts. To the extent that the targeted energy savings are not realized, the amount due from the client to the ESCO under the contract is reduced accordingly. Energy savings could be certified through a monitoring and valuation protocol based on the International Performance Measurement and Verification Protocol (IPMVP) to ensure transparency in the process.

- Due to the potential variability of the cashflows under such contracts due to performance risk, banks in Brazil are reluctant to accept them as the principal form of repayment and collateral. The other risk inherent in shared savings contracts is credit risk, i.e. failure of the client to make the scheduled payments for reasons other than technical underperformance.

- Table 5 illustrates a typical cashflow allocation under a typical shared savings contract. It is assumed that in such a contract the client retains at least 10% of the total energy savings amount. The next 75% of energy savings cash flow is used to service the bank debt, with the next 5% being used to recover the ESCO’s equity investment in the project investment costs (the amount not financed by the bank), and the final 10% being the ESCO’s profit. In the event that the actual energy saved is less than projected, the ESCO takes the risk of first losses for the first 15% of cashflow reduction. This amount is not guaranteed, creating an incentive for the ESCO to meet its maintenance obligations. In this example, the EE project would have to underperform by 15% to create a potential shortfall in cashflow available for debt service. This structure places a strong incentive on the ESCO to ensure that projected energy savings are realized, or lose income. It creates a strong incentive for the ESCO to quickly remedy any shortcoming in performance at the earliest possible moment.

- Typically, the shared savings contract would be pledged to the bank, and the cashflows controlled by the bank through a trust account. The first payments received into the account from the client would be dedicated to debt service. The surplus over debt service, assuming the EE project is achieving the projected savings, represents the ESCO’s cost recovery and profit, would then be released to the ESCO. Figure 1 illustrates a typical EE project financing structure including the intervention of the EEGM,

The EEGM

- Two key market barriers to the financing and implementation of local ESCO projects arise with respect to the lack of confidence by both end-users and lenders in the guaranteed energy savings projections provided by ESCOs.  The end-user market remains skeptical of energy savings guarantees provided by local companies, while local banks are not willing to consider energy savings as the principal collateral in assessing the credit-worthiness of an ESCO project.

- The main objective of the EEGM is to stimulate banks to rely on the cashflows generated by shared savings contracts as collateral for loans to ESCOs. Furthermore, the EEGM would also be able to issue a performance guarantee in favor of the client, to incentivize the client to enter into a contract with the ESCO in the first place.

- Creation of the EEGM should therefore address these market barriers by enhancing EE deal flow, with the objective of representing a major shift in local bank lending, away from exclusively balance sheet financing to project-based financing. Internationally, guaranteed energy savings provided by large ESCOs are accepted in the market due to their reputations and balance sheets. The EEGM should contribute to providing the same benefits to Brazilian ESCOs. A successful track record by the EEGM in support local ESCOs should, by its demonstration effect, address the restrictive lending environment in Brazil, the lack of experience with EE cashflow lending, the lack of awareness of the benefits of EE projects  by decision-makers in companies, lenders, and government institutions and the limitations of local ESCOs to meet high collateral requirements of local lending.

- The EEGM is a USD25 million guarantee facility, under which the IDB will provide its AAA-rated balance sheet to act as Guarantor of Record. The USD 25 million facility will be backstopped by a USD 10 million GEF grant  complemented with an additional USD15 million in balance sheet capacity from the IDB. If available, additional amounts of funding from other donors might be sourced subsequently to expand the size of the EEGM. The GEF funds will assume a first loss position in relation to the IDB’s exposure. The level of guarantees to be made available under the EEGM was established in consultation with most stakeholders, based on their experience and the size of the market in Brazil.

- Under the EEGM, the IDB will be able to issue various types of guarantee (see below) during a 5-year availability period, as long as the maximum outstanding liability under the program, at the time of guarantee issuance, is limited to USD25 million and the IDB’s own exposure (net of coverage by the pledged GEF deposit) is limited to USD15 million. ESCOs wishing to become eligible for consideration of support by the EEGM will be assessed against a set of eligibility and credit criteria to be determined by the IDB and the Administrator of the EEGM in advance of launching the facility.

- Projects recommended to receive a guarantee will be rated against a specific set of criteria including, but not limited to: (i) limited guarantee period of 7 years (the expected average period being 5 years); (ii) only established and proven types of projects/technology will be eligible; (iii) the EE-related project investment bracket will vary initially from a minimum of USD250,000 to a maximum of USD750,000, and (iv) credit criteria linked to the financial capacity of the ESCO’s client to make the required payments. While these limits and criteria will be adjusted based on development and experience of the EEGM, the bracket range would encourage adoption of an integrated approach.

- To ensure the continual relevance of the EEGM, the set of criteria will be continuously evaluated and adjusted as required during implementation of this component of the project.

Risks guaranteed

- Subject to the approval of the IDB’s Board of Executive Directors, which approval will be sought following the GEF CEO endorsement, the EEGM would offer IDB guarantees to assist ESCOs to move along their respective growth trajectories and meet their specific needs. The guarantees will cover two basic types of risk:

- Performance risk (cash flows from clients under performance based EE Contracts are insufficient to cover debt service to commercial banks, due to technical underperformance);

- Comprehensive risk (as described above, but covering both performance risk as well as credit risk, i.e. bankruptcy or financial incapacity of the client to make the required payments);

Application of guarantees

- The EEGM will be offered in the market with a collaboration agreement with BNDES in order to complement the use of PROESCO. The EEGM will also be capable of delivering guarantee solutions outside of PROESCO, to the extent that PROESCO does not fulfill the need.

- As mentioned above, the IDB guarantees to be issued under the EEGM are designed to be used in conjunction with BNDES’s PROESCO program, which currently provides low-cost funding to intermediary banks and assumes up to 80% of the risk of the loans made by the banks. Under PROESCO, commercial banks may also receive BNDES funding and assume the project risks themselves, which they may mitigate with alternative credit enhancements if available.  To encourage commercial banks who may be unwilling to accept the residual 20% risk, co-financing guarantees under the EEGM of up to 20 percent of commercial bank loans to ESCOs for projects in buildings may be issued directly in favor of commercial banks participating in the PROESCO program. In order to ensure risk sharing by the commercial banks, it is proposed  that co-financing guarantees covering comprehensive project risk will be issued for up to 10-15 percent (or up to 90-95 percent risk cover when combined with PROESCO). Co-financing guarantees of up to 20 percent (or up to 100 percent cover when combined with PROESCO) could be performance guarantees covering only the technical performance risk of the financed project, since the commercial bank would retain the credit risk for its own account. The EEGM’s guarantees may also be applicable to commercial banks willing to accept BNDES funding under PROESCO and mitigate project risks with alternative credit enhancements.

- It is expected that significant operational synergies may be achieved by a well-structured alliance between the EEGM and BNDES’s PROESCO program. For example, the technical evaluations and due diligence by BNDES and the EEGM’s Administrator (see below) are expected to be shared between the two institutions as well as with the commercial bank beneficiaries of PROESCO, primarily to assist the commercial banks in evaluating and understanding the technical risks involved in EE project financing using energy savings contracts as the main source of collateral.

- Performance guarantees may also be issued directly in favor of clients of the ESCOs, where the client is able to finance the EE project itself with debt or equity, but wishes to mitigate the risk of the ESCO not honoring its guarantee to provide a minimum amount of energy savings. The ESCO would pay for the guarantee and sign a reimbursement agreement with the IDB, in order to induce the client to sign the EE Contract. In this scenario, the performance guarantee would backstop EE project amounts equivalent to the client’s guaranteed share of the energy savings, usually of at least 10 percent of project costs.

- It is expected that performance or commercial guarantees for discounting operations may be relevant in the case of self-financing ESCOs growing their portfolios and willing to request commercial banks to discount their receivables. This will allow growing ESCOs to recycle their capital or reduce their exposure in order to implement additional project investments required for them to grow prior to them becoming eligible for commercial bank financing under PROESCO or as an interim funding product prior to PROESCO becoming fully operational. The discounting could be with full recourse to the end-user in the event of non-payment due to the end-user’s financial incapacity or bankruptcy, and with limited recourse to the ESCO only for non-payment due to technical underperformance of the EE project.

- In the event PROESCO does not become fully operational as quickly as planned, or in circumstances where commercial banks receive BNDES funding under PROESCO but are willing to assume project risks themselves and find alternative credit enhancements, the comprehensive risk or performance risk guarantees may be used as an alternative risk mitigation product for the commercial banks. As the EE market progresses and banks begin to accumulate significant portfolios of EE financings of any of the types mentioned above, the EEGM may be called upon to issue comprehensive risk portfolio guarantees to commercial banks. It is anticipated that this product would not be offered initially by the EEGM due to the early stages of development of EE project financing in Brazil, but could be approved for future marketing at the relevant time following a periodic review of the EEGM’s product menu.

Periodic Review of the EEGM and Alternative Applications

It is proposed that the EEGM and its menu of guarantee products should be reviewed periodically to ensure the relevance and acceptance of the program in the market. In order to remain as flexible as possible, the two categories of risk guarantees (comprehensive and performance) should remain available, but new applications of these guarantees may emerge or be required in light of the evolution of the market. For example, in the event that commercial banks are not sufficiently catalyzed to lend to EE projects as a result of the PROESCO and EEGM intervention, other types of financial intermediaries in the Brazilian capital markets may be sought, such as special purpose vehicles known as FDICs, which issue rated securities to investors and may use the funds raised to on-lend for specific purposes, in this case to ESCOs. If commercial banks do not access PROESCO with satisfactory volumes of business, BNDES funds available under PROESCO might be deployed to ESCOs for projects less than BRL10 million via a FDIC. Under this structure, BNDES would invest PROESCO funds in the FDIC and the EEGM guarantee would be granted in favour of the FDIC for the loans made by it, rather than to a commercial bank. This structure would require the consent of BNDES and the upfront costs, or part thereof, of setting up such an alternative intermediation structure could be funded by the GEF deposit at the relevant time.

EEGM Administrator

- The EEGM shall be managed by an experienced Administrator to be located in Brazil, expected to be a company or individuals with significant technical experience in EE projects and a good knowledge of the Brazilian financial markets. The role of the Administrator may also involve a coordinating entity or person which would outsource the relevant technical and financial expertise as and when needed. The Administrator will be selected by the IDB with involvement of the UNDP and the NPSC through competitive bidding and appointed after approval of the EEGM by the IDB’s Board of Executive Directors. The Administrator will be in charge of ensuring that the EEGM is delivered according to legal, commercial and financial criteria, which will be established with the selected Administrator. The Administrator will originate, perform technical evaluation and due diligence, (if applicable in the case of co-financing guarantees with PROESCO, in close coordination with BNDES) and will structure the guarantees according to pre-agreed eligibility and credit criteria and will request IDB to issue the guarantees.  Following receipt of a request for guarantee issuance from the Administrator, the approval and issuance of guarantees by the IDB would be done on an expedited and streamlined basis, assuming that the request complies with the eligibility and credit criteria. Documentation of the guarantee, including the signing of reimbursement agreement by the ESCO, will also be coordinated by the Administrator.

- The Administrator will also monitor the exposure of the portfolio, if necessary requiring the ESCO to remediate the shortfalls in energy savings (if any), and will exercise the IDB’s step-in rights to remediate the deficiency if the ESCO fails to remediate shortfalls in energy savings.

- If necessary will request the IDB to disburse under guarantees that are called by their beneficiaries. The Administrator will also be required to pursue recovery on behalf of the IDB. The IDB would have full authority to remove the Administrator for failure to reach certain pre-established performance criteria or for breach of any obligations that would be set out in the relevant contract between the IDB and the Administrator.

- The exact remuneration structure of the Administrator will be developed during the selection process. If necessary, the remuneration of the Administrator, and other operating costs including but not limited to the expenses of the IDB for monitoring visits and applicable trustee fees for the bank holding the GEF deposit, or part thereof, may be funded by the GEF deposit. The remuneration structure for the Administrator, depending on the results of the selection process, which will include as key selection criteria the remuneration structure proposed by the candidates, may involve a fixed monthly fee as well as additional performance-based variable fees such as a share of the interest earned on the GEF deposit.  If funds are drawn from the GEF reserve account to cover claims against outstanding guarantees, interest income on the reserve account will necessarily decline resulting in a reduction in the performance bonus.  This arrangement ties payment to the Administrator to performance of the program and creates a strong financial incentive for the Administrator to perform at the highest level.

EEGM Pricing

- Each type of guarantee issued under the EEGM may have different pricing based on its risk profile and the risk mitigation measures built in to it. It is expected that initially the Administrator will be able to offer a range of pricing, taking into account the risk profile of the individual EE project. In all cases, the IDB will receive a market return for the portion of the risk taken by the IDB, consistent with its second loss position. Pricing may vary over time based on market conditions and on the performance of the EEGM’s portfolio. The pricing ranges that may be offered by the Administrator will be reviewed periodically and adjusted according to certain pricing principles, which are expected to include: a) pricing levels must be referenced to historical or projected default rates for the relevant product; b) pricing should conform to relevant benchmarks such as other EE project risk mitigation programs such as PROESCO itself but also those in other countries offered by Multilaterals such as the Word Bank Group, including the IFC; c) pricing should reflect the risk margins charged by commercial banks without (or for the residual risk uncovered by) the guarantees, provided that the risk margin is rational and based on a realistic level of understanding of the risk. Finally, the pricing of the guarantee premium payable to the IDB should reflect the second-loss risk position of the IDB by way of a discount of the pricing factors mentioned in a) to d). The range of pricing to be offered during the first 12 months of the EEGM will be established shortly before the launch of the facility, based on market conditions and other relevant benchmarks prevailing at that time.

Table 5:  Example of a typical EE project under the EEGM

EEGM and role of the Government

- It should be noted that the EEGM is designed as a financial mechanism without recourse to the Government of Brazil nor is the Government liable to repay the GEF deposit. The guarantees to be issued by the IDB under the EEGM are to be granted under the IDB's Non Sovereign Guaranteed (NSG) window. Operations done by the Bank under this window may not benefit from sovereign guarantees. The risk that the IDB takes in this project is solely against a) the GEF deposit for first losses and b) thereafter, against the ESCOs who are liable to repay the IDB in the event of disbursements under the guarantees.

EEGM Exit strategy

- The exit strategy for the EEGM will be decided by the IDB, UNDP and the NPSC based on the EEGM’s uptake and relevance over the years. While the final maturity of guarantees outstanding under the EEGM and backstopped by the GEF deposit could be as long as 12 years, in principle, options for exit strategies relating to the residual GEF deposit could be reviewed, evaluated and decided upon by the IDB, the UNDP and the NPSC well before final maturity of the program.

- Options for exit strategies include the following:

(i) 	Extension of the EEGM if the mechanism has been successful. At the end of the 5-year guarantee issuance availability period, the IDB could request the GEF to extend the program and continue issuing guarantees with tenors extending beyond the original 7 year tenor and 12-year final maturity. Based on the historical default rates of the guarantee portfolio, the IDB might also consider increasing its contribution to the EEGM from the current USD15 million.

(ii) 	At the final maturity of the last guarantees issued under the EEGM, the residual GEF deposit could be returned to the GEF and/or the Brazilian authorities, to be recycled into new projects or to be used for technical assistance operations at the time. Indeed, to the extent there is a surplus of GEF funds on deposit in excess of the IDB’s maximum guarantee liabilities outstanding during the amortization period, surplus amounts could be released before the final maturity of the last outstanding guarantee.

(iii)	Another option would be to privatize the EEGM, assuming it is successful, by replacing the IDB as guarantor with a private sector institution, to be selected by the IDB, the UNDP and the NPSC, assuming that any guarantee beneficiaries outstanding at the time of the decision were agreeable to the change in guarantor. In this case, the residual GEF deposit would remain pledged to the new guarantor, which might be willing to extend the availability period for guarantee issuance, and the guarantee tenors

- To avoid that GEF funds are not misused, the option that we assume would need to have safeguards is option (iii), in which the IDB as guarantor is replaced with a private sector institution. This institution would be selected by the IDB, UNDP and the NPSC in a competitive tendering process.  Apart from the usual integrity checks that IDB makes on its clients, other selection criteria are having relevant technical expertise and have the guarantee capacity to be proposed by private sector applicants in relation to the residual GEF deposit amount, but that also have a long term interest as market player in seeing the efficiency market develop (are engaged having a long term view and are willing to use the funds to further the industry).

Outputs and corresponding activities will include:

- EEGM has been experimented and is fully operational. Design and implementation of a new financial mechanism based on performance guarantee including operational rules and management structure.

- Local banks begin to treat energy savings as collateral in their lending evaluation matrix. This output will be achieved based on the success in the implementation of EE projects financed with the guarantees of the EEGM.

Table 6	Budget, component 4

Outcomes 5 and 6: Project management and M&E implemented

- The overall management of the project will be the responsibility of the National Project Steering Committee (NPSC) that will be composed of senior representatives from the Ministries of Environment, Mines and Energy, Finance, and Public Planning, as well as national banks and the private sector.

- A National Project Management Unit (PMU) would oversee the administration of activities related to project outcomes 1-3. The PMU would have full-time staff members managed by a National Project Manager and an Assistant who would clear the work plan (which forms the basis for project execution), monitor activities, manage the project on its day-to-day implementation and report back to the Project Director. Project Steering Committee (PSC). The PMU will:

- Launch project activities.

- Develop the Request for Proposal for all the TA activities to be conducted by external organizations.

- Manage the project on a day to day basis.

- Produce all the management reports for the benefit of the Brazilian government, the GEF and UNDP.

- With respect to Outcome 4, the IDB working with local banks, ESCOs and the EEGM Administrator will establish guarantee criteria and procedures.  Once the EEGM is in operation, guarantee approval by the IDB will be streamlined assuming that the criteria for guarantee issuance have been met by the Administrator.  The IDB would have full authority to remove the EEGM Administrator for failure to reach certain pre-established performance criteria or for breach of any obligations that would be set out in the Administrator’s contract.

Table 7	Budget, monitoring and evaluation

| Monitoring and evaluation | Units | Cost/unit | GEF | Co-financing |
| --- | --- | --- | --- | --- |
|  |  |  |  |  | In cash | In-kind |
| Int'l consultants | 176 | days | 698.67 | 122,967 |  |  |
| Nat. consultant | 176 | days | 399.25 | 70,267 |  |  |
| Travel |  |  |  | 35,000 |  |  |
| Misc and professional services |  |  |  | 35,267 |  |  |
|  |  |  |  | 263,500 |  |  |

More details on management, monitoring and evaluation are given in Parts III and IV of this Section of the project document.

Table 8	Budget, project management

  - Project Indicators, Risks and Assumptions

- The “Market Transformation for EE in Buildings” project seeks to achieve several goals, and its success will be assessed against the following set of key indicators:

- Reduction in GHG emissions resulting from the improvement of electricity consumption in both public and private building facilities;

- Gradual elimination of substances that deplete the ozone layer, as supported by the MLF.

- As in many countries, a large part of electricity consumption goes to buildings. In Brazil this was estimated at 44% in 2004. As a result of increases in fossil fuel prices on the international market during 2005, the country’s energy sector policy seeks to enhance support for uptake of energy efficiency measures, mainly in the commercial, industry and institutional building sectors. Secondary indicators have also been included as they are central to the sustainability of this project. These are all linked to the project’s outcomes and include: (i) increased capacity of market actors; (ii) increased market activities related to EE project development and implementation in the public and private buildings sectors; (iii) increased financing leveraged as a result of establishment of the energy savings EEGM; and, (iv) an increased number of CFC-free chillers installed within the context of an integrated approach to adoption of EE measures.

Indicators

- Key outcome-level performance indicators used to justify the Objectives ratings during project development have been identified on a preliminary basis, as follows.

- Cumulative direct GHG emissions reduction: 2.01 million tCO2-eq over the next 20 years; post-project direct emission reduction and indirect emission reduction of 16.06 million tCO2.

- Key outcome-level performance indicators used to justify the Implementation Progress (IP) ratings during project development have been identified on a preliminary basis as follows:

- 5,000 service and equipment providers (design engineers, ESCOs, entrepreneurs and vendors) are informed or trained on buildings EE management;

- Some 250 EE projects  implemented supported by the EEGM  with a total investment value of USD 93.2 million and savings of savings over the first 5 years of USD 125 million

- Feedback on quality and relevance of project’s technical assistance (80% of beneficiaries of capacity   building activities rating them as “very good”);

- Number of stakeholders reached through dissemination of project publications/guides (at least 2,000);

- Number of visitors to the project web site (at least 1,000 per month in 6 months after website launch)

- Capacity building provided to public building organizations on the use of the PBI;

- PBI design and implementation of demonstration activities completed;

- 120 professionals trained in CFC-based chillers replacement with EE CFC-free chillers;

- Up to 40 chiller replacement demonstration projects completed using MLF co-financing.

Assumptions

- The following are conditions or factors that could assist the Project in achieving its objectives:

- The government entities involved in the Project are committed to adopt an appropriate legal and regulatory framework for EE promotion and CFC-based chillers replacement;

- Relevant participants, particularly co-funding agencies and companies, are committed to participating in various activities;

- Building owners/operators, especially in Brazil’s larger urban centers, are aware of and support, through increased participation, the demonstration pilot programs to improve EE efficiency in public sector and replace CFC-based chillers ;

- Line ministries are prepared to integrate the project strategy within their global and sectoral programs;

- The private sector is prepared to follow the government’s lead in participating at various levels (financial, technical, technological, etc.) to the Project’s realization;

- Local financial institutions (FIs) are interested in expanding their EE lending portfolios to support market transformation costs.

Risks

- Based on the meetings held in Brazil with the various stakeholders during the development of the present project, several potential risks have been identified. The following section briefly summarizes and assesses these risks briefly.

- The risk of lack of support for the PBI program within the Federal Government’s administration: The project has already taken steps to mitigate this risk by involving all relevant stakeholders in the design and preparation of the proposed project. It will continue to mitigate this risk by establishing a National Project Steering Committee (NPSC) to co-ordinate project activities with other ongoing activities in Brazil, as well as to discuss and introduce the legal and regulatory changes needed to promote energy efficiency incentives. This risk is assessed as low.

- Interest in EE financing does not evolve as projected during the PDF B phase: The creation of the EEGM in support of ESCOs is expected to spur interest in EE financing and lend support to development of EE projects.  A high level of interest has been expressed by national stakeholders with respect to the innovative nature of the guarantees to be made available under the EEGM during the PDF B phase.  The EEGM, properly designed and executed in Brazil, is expected to catalyze all levels of stakeholder interest in EE projects. This risk is assessed as medium to low.

  - Incremental reasoning; expected global, national and local benefits

- The current market opportunities for EE projects are limited due to a lack of confidence by both the end-user and the lender in the guaranteed energy savings projections provided by ESCOs. Local banks are not familiar with the performance risk associated with energy savings projects and are not willing to consider energy savings as collateral. In addition, EE opportunities in the public sector market are very limited due to existing procurement and contractual barriers.

- Therefore, it is reasonable to assume that, in the absence of the project’s interventions, Brazil’s EE efforts would likely remain in their current state or, given the reforms presently underway in the sector, funding for EE enhancement may start to decline as deregulation of the energy sector advances. Under the baseline scenario, demonstration of emerging technologies and market driven EE delivery mechanisms would be restricted. Investments in EE would most likely remain in Government hands, through the use of subsidized loans to state governments and qualifying enterprises.

- The total CO2 reduction directly attributable to the proposed GEF initiative is 2.01 million tonnes of CO2 equivalent over the 20 years of the equipment’s life. The post-project and indirect CO2 emission reduction due to replication is an estimated 16.06 million tCO2-equivalent over a ten-year period, giving a total emission reduction of 18.07 million tCO2.

- The global benefits of the project involve both reduction of GHG emissions and phase-out of the use of CFCs, thereby demonstrating cross-convention synergy potential amongst multilateral Environmental Agreements (MEAs). Improving EE in building operations will contribute to lowering GHG emissions from an energy consumption perspective, as well as through the reduction of CFC emissions which have a very high global warming potential.

- Nationally, endorsement and adoption of this project would position Brazil as one of the front leaders in the area of market transformation for energy efficient technologies, with wide-ranging applications and replication potential, both to other appliances and equipment, as well as in- and outside of Brazil. Additional national benefits include benefits to the local energy efficiency service industry, as well as a development of accessible financial mechanisms for local market players.

  - Country ownership: country eligibility and country drivenness

Country Eligibility

- According to the Instrument for the Establishment of the Restructured Global Environment Facility, Brazil qualifies for GEF financing on the following grounds:

- It has ratified the United Nations Framework Convention on Climate Change on 28-02-1994;

- It receives development assistance from UNDP’s core resources;

- In addition, Brazil ratified both the Vienna Convention for the Protection of the Ozone Layer and the Montreal Protocol on Substances that Deplete the Ozone Layer in March 1990. It has also subsequently ratified the Montreal Protocol’s London Amendment in October 1992, the Copenhagen Amendment in June 1997, and the Montreal and Beijing Amendments in June 2004.

Country Drivenness

- The Government of Brazil began adopting policies and measures with stronger emphasis on energy efficiency over two decades ago. Programs have been implemented at the federal, state and municipal levels, as well as in the private sector. The overview of ongoing EE programs in Brazil, given in Part 2 of Section A, underlines the Government’s interest in EE promotion and adoption.

- The PROCEL (Programa Nacional de Conservação de Energia Elétrica) was initiated in 1985. Under Eletrobras responsibility since 1998, the program’s objectives are to promote the rational use of electricity by, inter alia, households, industry, water utilities and public buildings, and public lighting;

- The CONPET program, created in 1991, aims at encouraging the efficient use of oil products and natural gas in the transport, commerce, industry and agriculture sectors;

- Law # 9991 of 24 July 2000 mandates electricity distribution companies to invest in research and development (R&D), and in EE programs. Companies are required to apply annually, as a minimum, the amount of 1% of their operational liquid income to R&D for the electric energy sector, including a minimum of 0.5 % in programs geared at EE for end users, referred to in Brazil as the ‘ANEEL Fund. ANEEL (Agencia Nacional de Energia Eletric) was created by Law 9427 (1996) and is part of the Ministry of Mines and Energy (MME). ANEEL regulates and inspects the production, transmission, distribution and commercialization of electric energy in Brazil.  A percentage of the annual revenues of utilities needs to be used for specific public-benefit investments, including energy efficiency

- Under the Brazilian Labeling Program (PBE), established in 1983 and managed by INMETRO, Brazil applies a voluntary labeling scheme for energy consuming equipment. Beginning in 2006, labeling is now mandatory for a variety of equipment. Labeling has proven to be very effective in terms of encouraging market transformation elsewhere. In association with the PBE, PROCEL has created an award for the most efficient electric products in the market for each type of equipment. Both, the PBE and PROCEL labels serve as marketing tools for manufacturers. Parallel to PBE, Law 10.295 (October 2001) stipulates that minimum EE or higher EE standards are to apply to energy consuming equipment and buildings in the future.

- The EDIFICA Program (Programa de Eficiência Energética em Edificações) - EE Program for Buildings), under PROCEL Management since 2003, is responsible for organizing actions and setting targets for improvements that would lead to the development of: (i) establishing minimal requirements to integrate the architecture of buildings to the environment and to natural resources; (ii) creating EE indicators for buildings; (iii) certifying material and equipment and establishing procedures for regulation/legislation; (iv) creating mechanisms to provide financial resources and the removal of barriers to the implementation of projects; and, (v) promoting educational and social interest projects.

- On top of the aforementioned initiatives, BNDES, the national development bank in Brazil, has launched a new financing mechanism, a partial credit risk guarantee initiative (PROESCO) that will aim at reducing the risks for banks in taking an active part in the EE market in the country (as discussed under Outcome 4)

  - Sustainability and replicability

Replicability

- By end of the project, the conditions created by its implementation should encourage project developers, financing institutions and building owners/operators to replicate EE projects. The market will have been primed, the deal flow enhanced and private sector interest in this mechanism will be established. It is expected that the EEGM will be replicated by other financial players, such as insurance companies, that will benefit from the project experience and accomplishment to create and scale-up a sustainable performance guarantee market. More broadly speaking, by demonstrating success, either one or both of the newly developed activities could be used in other countries with similar economic situations.

Sustainability

- The use of market mechanisms to promote the development of EE initiatives holds the best prospect for sustainability, as it allows market actors to make decisions based on commercial merit. In addition, where market imperfections may be present, well-designed interventions can be very effective in bringing the market to the level required for normal and effective market operation.

- Institutional. A major change expected to result from the project’s implementation will be to enable public sector building managers to have access to outsourcing of technical and financial services all over the country.  The PBI component will develop and market all necessary tools to reach that objective. As similar successful initiatives in other countries have been implemented, the project will take advantage of these experiences in designing and implementing the appropriate tools.

- Technical. A Capacity Building component will be made available to a large number of stakeholders including building owners and operators, to all kind of EE service and equipment providers, including ESCOs, as well as to other key partners including universities and technical educational institutions. The new capacities created through this initiative are expected to be applied over time.

- Financial. EEGM is designed to be financially self-sustainable and operated by a private company with a performance based incentive compensation system. The appropriate flexibility to adjust to market level components, such as project eligibility criteria and service fees, will result in financial services mechanisms adapted to market conditions. EEGM will encourage local financing institutions to accept energy savings guarantees as collateral, reducing the high collateral requirements currently imposed by local banks on ESCO projects in Brazil.

- Socio-economic.  ESCOs currently exist in Brazil but it will be greatly reinforced by the present project, making it more viable. ESCOs will be one of the major players who actually benefit from the project by increasing the number of EE projects implemented.

- Management Arrangements

The project will be executed in accordance with standard UNDP execution guidelines.

- The executing agency will create, in consultation with UNDP, a National Project Steering Committee (NPSC) that will be established to oversee the global implementation of the project during its entire execution. The NPSC will be composed of senior representatives from the Ministries of Environment, Mines and Energy, Finance, and Public Planning, as well as national banks and various private sector interests (refer to Stakeholder Involvement section).

- A national Project Management Unit (PMU) that will manage and supervise the global implementation of the project during its entire duration, except for Outcome 4 - the EEGM, will be established with specific emphasis on the management of the PBI and the capacity building activities of Outcome one. The PMU would have full-time staff members managed by the Project National Coordinator, in coordination with a Project Technical Manager hired by the Project, who with the support of an assistant will review proposals, clear the work plan (which forms the basis for project execution), monitor activities, manage the project on its day-to-day implementation and report back to the National Project Director (at the Ministry of Environment) and the Project Steering Committee.  The Ministry of Environment will be the leading executing agency, in partnership with the Ministry of Mines and Energy (MME), for project implementation, except for Outcome 4 given the peculiarities of the EEGM administration detailed previously in this document.

- The EEGM facility, under the oversight of IDB, will be managed by a separate and qualified Administrator, engaged through a competitive international recruitment process. The EEGM Administrator will be staffed by highly trained and experienced technical and financial experts with extensive experience in the ESCO industry. This service would be performed under a management contract. The administrative and financial procedures of the EEGM will be established on the basis of IDB experience and due diligence. Furthermore the IDB will oversee the activities of the EEGM ensuring its transparent performance.

Figure 2	Project implementation structure

- UNDP will have the overall responsibility of the project implementation with particular emphasis on the capacity building activities of outcome 1 and 2 and the implementation of outcome 3 but it will also play an active role in the implementation of outcome 4 under the oversight of IDB.

- In order to accord proper acknowledgement to GEF for providing funding, a GEF logo would appear on all relevant GEF project publications. Any citation on publications regarding projects funded by GEF should also accord proper acknowledgment to GEF. The UNDP logo should be more prominent -- and separated from the GEF logo if possible, as UN visibility is important for security purposes.

- Monitoring and evaluation

- Project monitoring and evaluation (M&E) will be conducted in accordance with established GEF procedures as well as following new UNDP procedures in the ATLAS system.  Project M&E provided by the project team, supported by UNDP, i.e., the UNDP Country Office (CO) and the UNDP-GEF Regional Coordinating Unit (RCU). The Logical Framework Matrix in Annex B of the Executive Summary provides performance and impact indicators for project implementation along with their corresponding means of verification. These will form the basis on which the project's Monitoring and Evaluation system will be built throughout the implementation period.

- The main components of the Monitoring and Evaluation Plan will include: (1) establishing monitoring responsibilities and events, (2) project reporting and (3) independent evaluations. The project's Monitoring and Evaluation Plan will be presented and finalized at the Project's Inception Report following a collective fine-tuning of indicators, means of verification, and the full definition of project staff M&E responsibilities. Project monitoring and evaluation will be conducted in accordance with established UNDP and GEF procedures and will be provided by the national project team and the UNDP Country Office (UNDP-CO) with support from UNDP/GEF. The project indicators, as given in the Project Logical Framework, are the benchmark against which Monitoring and Evaluation will take place.

- The EEGM monitoring will be carried out by the IDB through the reports of the Administrator and will make them available to UNDP and the NPSC. The IDB will have the right to review the operations and financial records of the Administrator and to appoint a independent auditor for the purposes of performing an audit on the books of the Administrator, to inspect the procedures used to recover guarantees disbursed due to defaulted projects and to review the operations of the Administrator for the purpose of developing and enhancing best practices and implementing improvements based on the Administrator’s record. The IDB will apply the same degree of care and diligence in the execution of its responsibilities herein as it exercises in the monitoring of its private sector projects.

Monitoring and Reporting

Project Inception Phase

- A Project Inception Workshop (IW) will be conducted with the full project team, relevant government counterparts, co-financing partners, the UNDP-CO and representation from the UNDP-GEF Regional Coordinating Unit, IDB as well as UNDP-GEF (HQ) as appropriate. The fundamental objective of the IW will be to allow the national project team to take ownership of the project’s goals and objectives, as well as finalize preparation of the project's first Annual Work Plan (AWP) on the basis of the project's log frame matrix (indicators, means of verification, assumptions), and in a manner consistent with the expected outcomes for the project.

- The Annual Project Work plan (AWP) will describe in detail the provision of inputs, activities, and expected results for the project in a given year, indicating schedules and the persons or institutions responsible for providing the inputs and producing results. The AWP will be updated and revised each year by the project manager in consultation with stakeholders and the UNDP-CO.

- Additionally, the IW will: (i) detail the roles, support services and complementary responsibilities of the UNDP-CO vis-à-vis the project team; (ii) fine-tune the specific targets for the first year implementation progress indicators together with their means of verification. These will be used to assess whether implementation is proceeding at the intended pace and in the right direction and will form part of the Annual Work Plan. Targets and indicators for subsequent years would be defined annually as part of the internal evaluation and planning processes undertaken by the project team; (iii) define means of measuring impact indicators related to global benefits. The measurement of global benefits will be undertaken through subcontracts or retainers with relevant institutions or through specific studies that are to form part of the project’s activities; (iv) provide a detailed overview of UNDP-GEF and GEF specific reporting and monitoring and evaluation (M&E) requirements, with particular emphasis on the Annual Project Implementation Reviews (PIRs), the Annual Project Report (APR), Tripartite Review Meetings (TPR), as well as mid-term and final evaluations; and, (v) provide an opportunity to inform the project team on UNDP project related budgetary planning, budget reviews, and mandatory budget re-phasing.

- The IW will also provide an opportunity for all parties to understand their roles, functions, and responsibilities within the project's decision-making structures, including reporting and communication lines, and conflict resolution mechanisms. The Terms of Reference for project staff and decision-making structures will be discussed and finalized in order to clarify each party’s responsibilities during the project's implementation phase.

Monitoring responsibilities and events

- A detailed schedule of project reviews meetings will be developed by the project management, in consultation with project implementation partners and stakeholder representatives, and incorporated in the Project Inception Report (IR). Such a schedule will include: (i) tentative time frames for Tripartite Reviews, Steering Committee Meetings, (or relevant advisory and/or coordination mechanisms) and (ii) project related M&E activities.

- Day-to-day monitoring of implementation progress will be the responsibility of the project manager, based on the project's Annual Work Plan (Strategic Planning Matrix) and its indicators. The PMU will inform the UNDP CO and MMA of any delays or difficulties faced during implementation so that the appropriate support or corrective measures can be adopted in a timely and remedial fashion.

- Periodic monitoring of implementation progress will be undertaken by the National Project Steering Committee (NPSC) through quarterly meetings with MME, IDB and UNDP (or more or less frequently as deemed necessary). This will allow parties to take stock and to troubleshoot any problems pertaining to the project in a timely fashion to ensure smooth implementation of project activities. UNDP Country Office and UNDP-GEF Regional Coordination Unit are responsible for monitoring the project activities on a continuous basis and can conduct, as appropriate, visits to the project and field sites to assess first hand project progress. IDB will be in charge of the overall monitoring of the EEGM as described in the Term Sheet of the mechanism. Any other member of the Project Steering Committee can also accompany, as decided by the Committee. A Field Visit Report will be prepared by the CO and circulated no less than one month after the visit to the project team, all NPSC members and UNDP-GEF.

- The Terminal Tripartite Review (TTR) is held in the last month of project operations. The project proponent is responsible for preparing the Terminal Report and submitting it to UNDP-CO, UNDP-GEF-HQ and IDB. It shall be prepared in draft at least two months in advance of the TTR in order to allow review, and will serve as the basis for discussions in the TTR. The terminal tripartite review considers the implementation of the project as a whole, paying particular attention to whether the project has achieved its stated objectives and contributed to the broader environmental objective. It decides whether any actions are still necessary, particularly in relation to sustainability of project results, and acts as a vehicle through which lessons learnt can be captured to feed into other projects under implementation of formulation.

Project Monitoring Reporting

- The project manager in conjunction with the UNDP-GEF extended team will be responsible for the preparation and submission of the following reports that form part of the monitoring process. Items (a) through (e) are mandatory and strictly related to monitoring, while (f) has a broader function and the frequency and nature is project specific to be defined throughout implementation.

a)  Inception Report (IR)

- A Project Inception Report will be prepared immediately following the Inception Workshop (IW). It will include a detailed First Year AWP, divided into quarterly time-frames, detailing the activities and progress indicators that will guide implementation during the first year of the project. The Report will also include the detailed project budget for the first full year of implementation, prepared on the basis of the AWP, as well as any M&E requirements to effectively measure project performance during the targeted 12 months time-frame.

- The IR will include a detailed narrative on the institutional roles, responsibilities, coordinating actions and feedback mechanisms of project related partners. A section on progress to date on project establishment and start-up activities and an update of any changed external conditions that may affect project implementation should be included.

- When finalized the report will be circulated to project counterparts who will be given a period of one calendar month in which to respond with comments or queries.  The IR is due at the beginning of project implementation.

b) Annual Project Report (APR) - Project Implementation Review (PIR).

- The APR-PIR is a UNDP and GEF requirement to facilitate central oversight, monitoring and project management. It is a self-assessment report by project management to the CO, providing inputs to the CO reporting process, as well as forming a key input to the UNDP/GEF M&E Unit, which analyzes the APR-PIRs by focal area, theme and region for common issues/results and lessons. The format of the APR is flexible but should include the following:

- An analysis of project performance over the reporting period, including outputs produced and, where possible, information on the status of the outcome;

- The constraints, if relevant, experienced in the progress towards results and the reasons for these;

- The AWP;

- Budget and full expenditure reports;

- Lessons learned;

- Clear recommendations for future orientation in addressing key problems in lack of progress.

c)  Quarterly Progress (QORs) and Financial Reports.  Short reports outlining main updates in project progress will be provided quarterly to the local UNDP Country Office (and forwarded to the UNDP-GEF RCU and IDB) by the Project Coordinator.

d)  Baseline and end-of-project reports.  During the inception stage the PMU will commission a study on the baseline situation. A similar study will be conducted done at the end of the project’s implementation to revisit the data and issues of the baseline study and to quantify the progress indicators of the logical framework of the project document.  This should enable the quantitative evaluation of outputs and impacts of the EEGM and capacity development interventions on EE uptake in buildings in Brazil in general.

e)   Project Terminal Report (PTR). During the last three months of the project the project team will prepare the Project Terminal Report (PTR).  This comprehensive report will summarize all activities, achievements and outputs of the Project, lessons learnt, objectives met, or not achieved, structures and systems implemented, etc. and will be the definitive statement of the Project’s activities during its lifetime.  It will also lay out recommendations for any further steps that may need to be taken to ensure sustainability and replicability of the Project’s activities.

f)  Project Reports and Publications. Project Publications will form a key method of crystallizing and disseminating the results and achievements of the Project.  These publications may be scientific or informational texts on the activities and achievements of the Project, in the form of journal articles, multimedia publications, etc.  These publications can be based on technical reports, depending upon the relevance, scientific worth, etc. of these reports, or may be summaries or compilations of a series of technical reports and other research.  The project team will determine if any of the Technical Reports merit formal publication, and will also (in consultation with UNDP, IDB, the government and other relevant stakeholder groups) plan and produce these Publications in a consistent and recognizable format. Project resources will need to be defined and allocated for these activities as appropriate and in a manner commensurate with the project's budget.

Independent Evaluation

The project will be subject to two independent external evaluations as follows:

Mid-term Evaluation

- An independent Mid-Term Evaluation will be undertaken at the end of the third year of implementation. The Mid-Term Evaluation will determine progress being made towards the achievement of outcomes and will identify course correction if needed. It will focus on the effectiveness, efficiency and timeliness of project implementation; will highlight issues requiring decisions and actions; and will present initial lessons learned about project design, implementation and management. Findings of this review will be incorporated as recommendations for enhanced implementation during the final half of the project’s term.  The organization, terms of reference and timing of the mid-term evaluation will be decided after consultation between the parties to the project document.

Final Evaluation

- An independent Final Evaluation will take place three months prior to the terminal tripartite review meeting, and will focus on the same issues as the mid-term evaluation.  The final evaluation will also look at impact and sustainability of results, including the contribution to capacity development and the achievement of global environmental goals.  The Final Evaluation should also provide recommendations for follow-up activities. The Terms of Reference for this evaluation will be prepared by the UNDP-CO based on guidance from the UNDP-GEF-RCU, UNDP-GEF and IDB.

Audit Clause

The Governments of Brazil will provide the Resident Representative with certified financial statements, as well as with an annual audit of the financial statements relating to the status of UNDP (including GEF) funds according to the established procedures set out in Section 30503 of the UNDP Policies and Procedures Manual (PPM) and Section 10404 of the UNDP Finance Manual.  The Audit will be conducted by the legally recognized auditor of the Government, or by a commercial auditor engaged by the Government.

Table 9:	 Indicative M&E work plan and budget

| Type of M&E activity | Responsible Parties | Budget USD | Time frame |
| --- | --- | --- | --- |
| Inception Workshop/ Annual Work Plan finalization | NPSC Project Team UNDP CO Hired consultant | 15,000 | Annually, first SPM immediately following approval of Phase II |
| Baseline Study of Project Indicators | PMU Hired consultant | 40,000 | Start and end of project. |
| Measurement of Means of Verification for Project Progress and Performance (measured annually) | Oversight by UNDP-GEF RCU & Project Management Counterpart organizations in the field or hired consultants on an as-needed basis | 0 | Annually prior to APR/PIR and to the definition of annual work plans |
| APR-PIR | PMU UNDP-CO UNDP-GEF | 0 | Annually |
| Steering Committee Meetings | NPD UNDP CO | 0 | Following Project IW and held regularly |
| Technical reports | PMU | As part of project activities | To be determined by Project Team & UNDP-CO |
| Mid-Term Evaluation | PMU Hired consultants | 45,000 | Mid project |
| Final External Evaluation | PMU UNDP-CO UNDP-GEF RCU External Consultants (i.e. eval. team) | 45,000 | At the end of project implementation |
| Terminal Report | NPD/PMU UNDP-CO | As part of project activities | At least one month before the project’s end |
| End-of-project impact study | PMU UNDP-GEF RCU (suggested formats for measuring impacts, etc) | 60,000 | Yearly |
| Lessons learned analysis and info dissemination | PMU UNDP-GEF RCU (suggested formats for documenting best practices, etc) | 27,500 | Towards the end of the project |
| Audits | UNDP-CO NPD/PMU | 31,000 | Yearly |
| Visits to field sites (UNDP staff travel costs not included as will be charged to IA fees) | UNDP CO UNDP-GEF RCU (as appropriate) Government representatives | 0 | Yearly |
| TOTAL indicative COST Excluding project team staff time and UNDP staff and travel expenses. | USD 263,500 |  |

- Legal context and other agreements

- This Project Document shall be the instrument referred to as such in Article I of the Standard Basic Agreement between the Government of Brazil and the United Nations Development Program, signed by the parties on 29 December 1964. The host country implementing agency shall, for the purpose of the Standard Basic Assistance Agreement, refer to the government co-operating agency described in that Agreement.

- The UNDP Resident Representative in Brasilia is authorized to effect in writing the following types of revision to this Project Document, provided that he/she has verified the agreement thereto by the UNDP-GEF Unit and is assured that the other signatories to the Project Document have no objection to the proposed changes:

- Revision of, or addition to, any of the annexes to the Project Document;

- Revisions which do not involve significant changes in the immediate objectives, outputs or activities of the project, but are caused by the rearrangement of the inputs already agreed to or by cost increases due to inflation;

- Mandatory annual revisions which re-phase the delivery of agreed project inputs or increased expert or other costs due to inflation or take into account agency expenditure flexibility; and

- Inclusion of additional annexes and attachments only as set out here in this Project Document.

COST RECOVERY POLICY

- As per Determination and Decision of the UNDP’s Executive Board on the Cost Recovery Policy over Regular and Other Resource-funded projects, the GEF contribution is subject to UNDP’s cost recovery as follows:

    - Direct Costs incurred in the provision of Implementation Support Services (ISS) by UNDP. These costs shall be unequivocally related to specific activities and transactional services clearly identified, charged as per standard service fees in practice.  These costs are an integral part of the project’s budget and shall be included in the activities’ budget lines corresponding to the services rendered.

- STRATEGIC RESULTS FRAMEWORK; GEF INCREMENT

- INCREMENTAL COST ANALYSIS

Table 10	Incremental cost matrix

| Cost/Benefit | Baseline (B) | Alternative (A) | Increment (A-B) |
| --- | --- | --- | --- |
| Domestic Benefits | Current level of energy savings in buildings remains low Current level for EE technologies, information dissemination, regulations, financing mechanism and capacity are limited No demonstration projects on EE CFC Free chillers replacement are implemented | The EE investments in the building sector under the proposed project will improve building operation and reduce energy bill. Building owners/operators, energy services providers and technology suppliers will also improve their capacity to manage energy resources, increasing the quality and reliability of EE services for public and private facilities. Banks will improve lending resources for ESCOs and EE project promoters. Domestic benefits would include reductions in local air pollution and reductions in fuel imports for electricity power generation. | Improved level of services and 4 million MWh of energy saved EE barriers removed Air pollution reduced and reduction of CFC usage in chillers |
| Global Environmental Benefits | In the baseline, investments in EE will result in limited reductions in fuel consumption in the public and private building sectors. Investments in EE will develop slowly based on the learning curve of the banking system and potential projects will go unrealized because of a lack of incentives to implement the projects and a lack of capacity among stakeholders to utilize bank credits. Current level of CO2 emissions remains high | In the GEF alternative 2.01 Mt CO2 are reduced through investments in energy-savings projects directly. Post-project emission reductions (due to the continuing operation of EEGM after the project’s end) are an estimated 8.03 MtCO2, while indirect emission reduction is also 8.03 MtCO2. Experts will provide a centralized source of training and assistance for the EEGM in EE building technology with an overview of the various sources of funding available, increasing the demand for credit resources. Barriers will be reduced or eliminated resulting in CO2 emissions reduction. There will have increase in the number of viable EE projects able to be replicated in the country and the region | Significant GHG emission reductions are attained. The cumulative CO2direct and post-project reductions (over the 20 years life of the technologies) are 10.4 million. Indirect CO2 emission reductions projected as a result of this project are 8.03 MtCO2 Total reduced CO2 emissions equal to 18.07 Mt CO2 eq over 20 years (see details of reduction calculations below) |
| Cost/Benefit | Baseline (B) | Alternative (A) | Increment (A-B) |
| Outcome 1: Enhanced EE investments through capacity building in EE in private and public buildings | Cost: 0.500 million A continued lack of capacity and awareness among stakeholders, energy services providers, equipment suppliers and financing institutions hinders the identification and implementation of EE projects. While some opportunity exists, the lack of knowledge first, in HVAC operation and other EE technologies, second in loan request preparation makes it difficult to achieve good result. | Cost: 1.868 million The project provides a technical assistance to train ESCOs, Equipment Suppliers, Universities, Building owners/operators to facilitate the development of a long-term stream of high-quality EE projects with diversified financing. Available funding is used more efficiently through capacity building of the EE market main actors to lead an increase in demand for EE services and the capacity for the ESCOs to respond to that demand. | Cost: 1.368 million (GEF) High-quality technical support to the ESCOs, Equipment Suppliers, Building owners/operators and Government entities and to energy users throughout the country. |
| Outcome 2: Access to EE services and commercial financing for public sector buildings enhanced with a PBI | Cost: 0.160 million The current purchasing mechanism for public sector is lowest cost only. | Cost: 1.343 million Introduction of a pilot program to improve EE in Public Building Sector. | Cost: 1.183 million (GEF) Model for PBI designed by half of first year. Public sector EE Program implementation |
| Outcome 3: Interest enhanced in the replacement of E-inefficient CFC-using chillers | Cost: 0.300 million (Montreal Protocol) While MLF funds feasibility analysis, the barriers to eliminate all the CFC still remain due to the difficulty to raise funds for this purpose. | Cost: 1.000 million The project provides a source of expertise and funding to launch a pilot project for the removal of up to 40 CFC-based chillers | Cost: 0.700 million (Montreal Protocol) The link with EEGM removes the financial barriers and more building owners are interested in replacing their inefficient chillers and carry out feasibility studies. |
| Outcome 4: EEGM made available to stimulate EE investment through ESCOs | Cost: 12.000 million EE financing remains a priority, but fund-raising is not targeted strategically or coordinated. Financing EE activities continues to be dominated by government grants, with continued low disbursement rates for available credits, as state organizations lack skilled personnel and experience of using loan resources to finance EE measures. Few ESCOs can borrow from commercial Banks; they use ANEEL fund and own money or partly client money. PROESCO has some lending in its portfolio fotr ESCOs and private sector, but remains small, facing the barriers mentioned above | Cost: 130.412 million EEGM led to a portfolio of energy saving projects with a high potential for replication. Projects also provide information on techniques that are particularly successful and cost-effective, and information on the projects can be shared with other potential investors. Particular emphasis is placed on the use of loan resources to stimulate cost-effectiveness of EE investments. Key barriers to investments in EE, such as a lack of well-prepared, bankable projects and a lack of awareness of the benefits of investments in EE, have been permanently reduced. | Cost: 118.412 million GEF: 10.195 million IDB: 15.000 million Beneficiaries/ESCOs: 93.217 million Improvement of quality of energy audits and feasibility studies related to EE systems and CFC-based chillers replacement in buildings. Enhancement of credibility of ESCOs benefiting EEGM guarntees, and thus access to financing via commercial banks. |
| Outcome 5, M&E | Cost: 0.0 million | Cost: 0.260 million | Cost: 0.260 million |
| Outcome 6: PM | Cost: 0.0 million | Cost: 1.387 million | Cost: 1.387 million GEF: 0.490 million; MMA (project management) and beneficiaries (management of investment projects): 0.897 million |
| Cost Totals | 12.960 million | 136.274 million | 123.314 million GEF: 13.500 million MP: 1.000 million IDB: 15.000 million Beneficiaries: 93.217 million (cash) In-kind (MMA): 0.414 million In-kind (beneficiaries): 1.143 million |

Emission reduction

- In order to make an evaluation of the carbon emission reduction that will be generated from the present project, a series of assumptions have been made:

Direct emissions reductions

- In a first step, the evaluation of the direct emission reductions was made on the basis that USD25,000,000 would be made available for the use of the EEGM (USD10 million from GEF and USD15 million from the IDB). The USD 25,000,000 will be dedicated to be used as a reserve against claims that will be done for not meeting the energy consumptions reductions guaranteed by the ESCOs. In order to evaluate the savings that could be generated from the projects to be guaranteed by the EEGM, it is assumed that the average project presented to the facility will need a total investment of about USD372,869 (including interest to be paid on the loan; see Table 5) and will generate at least USD100,000 of savings per year over the first 5 years. It is also assumed that the EEGM will only cover 90% of the default, the ESCO assuming the first 10% of non-attained savings.

- It is further estimated that about 250 projects over a period of can be covered by the EEGM over the 7-year UNDP/GEF project period. Based on an average of USD 0.125/kWh cost of electricity, a 20 years lifetime of the energy efficiency measures implemented, the EEGM would be able to generate 4.0 million MWh directly of savings. Using the grid emission coefficient for Brazil of 0.502 tCO2/MWh (as recommended in the publication titled ‘Brazilian Greenhouse Gases Emission Baseline from Electricity Generation) enables to evaluate the cumulative direct emissions reductions for the project at 2.008 MtCO2 (million tons of CO2-equivalent).

Direct post-project emission reduction

- Since EEGM will continue to operate after the close of the project, it is necessary to calculate the CO2 emission reduction that will stem from new investment after the project has expired. The funds size is initially USD 25 million. Correcting for some defaults (for which the PCGs have to be used) to fund will be available to guarantee further investments. Using a ‘turnover’ factor of ‘4’, the post-project direct emission reduction can be estimated at:

4 x 2.008 Mt CO2 = 8.032 MtCO2.

Indirect emissions reductions

- Indirect emission reduction can be calculated by assessing how many times the investments made during the project and direct post-project project direct impacts will be replicated (e.g. by increased awareness and capacity), not including the post- (mentioned above). Using the suggested replication default factor of ‘4’ for credit and guarantee facilities proposed by the ‘GEF Manual for Calculating GHG Benefits of GEF Projects’, the  indirect emissions reductions to be generated by the project are equal to:

0.8 x (2.008 + 8.032) MtCO2 = 8.032MtCO2.

Global emissions reductions

- Based on these figures, we can estimate that the global emission reductions to be generated by the present project are:

2.008 + 8.032 + 8.032 = 18.072 million tons of CO2

Cost for GEF per ton of CO2 avoided

13,500,000 /8.032 MtCO2 = USD 0.75 per ton of CO2

- STrategic results framework (SRF)

Table 11  Strategic results framework

| Project Strategy | Objectively verifiable indicators |
| --- | --- |
| Goal: | To influence, transform and develop the market for energy-efficient building operations in Brazil and move towards a less carbon-intensive and more sustainable energy consumption path in the country. With this project Brazil will significantly improve the general conditions in which EE measures are implemented in all economic sectors. Private and public building owners/operators will have the possibility to really take advantage of energy savings in their buildings with the technical and financial support of EE service companies such as ESCOs. |
|  | Indicators | Baseline (in the absence of the project) | Target | Sources of Verification | Risk and Assumptions |
| Project Objective: To foster EE investments in private and public buildings in Brazil. | Increase in the number and in annual revenues of EE project developers Rate of public and private building owners/operators reported to use ESCOs services to improve their energy consumption (at least 80%) Number of FI offering energy savings guarantee services other sources Number of new EE implemented projects using the EEGM or other similar mechanism due to the Project | Very few buildings owners/operators have incorporated EE measures Govt. buildings operation do not specify minimum EE performance values Professionals and developers do not understand basic EE principles Financing institutions are not aware on how they can support the development of EE market | Increase in investment in EE for building public and private sectors by USD93 million Local banking system provide financing in 70% of EE projects At least 10 FIs and value (at least $ 123M in total) of financed EE investment enabled by the Project, including by local FIs and At least 250 projects implemented, resulting in direct CO2 emission reduction of 2 MT CO2 and post-project and indirect 16 MT CO2. Improvement in kWh per m2 of building space | Bi annual progress report Independent mid-term evaluation Final Evaluation of the Project | Govt. adopts necessary institutional and regulatory framework Govt. is willing to “lead by example” in adopting EE promotion Plan in its own building Strong support from professionals and Banks for EE promotion |
| Outcome 1: Enhanced EE investments through CB in EE in private & public buildings | EE offer fully functional in private building sector EE offer fully functional in public building sector EE Product and Service providers trained | Limited capacity in term of EE offer from local market players | EE building market capacity building in progress by Yr 1 Efficiency Improvement in Brazil reinforced by Yr 5 | Project files Progress Reports Workshop evaluation reports | Political support to reinforce the EE market |
| Output 1.1: Local energy product/service providers capacity strengthened through training events | Number of stakeholders (building managers, entrepreneurs, equipment providers, ESCOs) advised or trained (up to 1400 product/service providers) Number of transactions supported by the Project’s TA services (more that 90) Feedback on quality and relevance of Project’s assistance (80% of beneficiaries rating “very good” the TA) | Limited capacity of EE product/service providers | 1400 ESCOs, Equipment providers, Building owner/managers association, Engineers associations, Technical Education institutions and Universities strengthened Project Management Unit set up by end of Yr 1 | Official govt. publication Meeting minutes Project Progress Report M&E Report | Gov. of Brazil support the EE project Professional in EE sector participate to project activities |
| Output 1.2: EE market players have greater awareness of and interest in implementing EE measures | Number of people from public and private building sectors trained (up to 5000 persons) Number of stakeholders reached with Project publications (at least 2,000) Number of unique visitors to Project’s Web site (at least 1,000 per month in 6 months after website launch) | Limited EE activities conducted by the Authorities on EE benefit for market players | Up to 5000 participants from public and private sector informed on the project benefit | Project files Official govt. publications Awareness campaign evaluation reports | Gov. of Brazil support the EE project Professional in EE sector participate to project activities |
| Outcome 2: Access to EE services and commercial financing for public sector buildings enhanced with a PBI | Public building EE tender process PBI Program for Public Building operational by end of project | The current purchasing mechanism for public sector is lowest cost only | Model for PBI designed by end of first year. Public sector EE Promotion plan drafted and submitted to the Gov. for adoption by the end of Yr 2 | Official govt. publications M&E reports | Govt. and Public entities willingness to incur additional cost of EE measures |
| Output 2.1: Enabling institutional framework for EE project development in Public Sector is established | Validation of the EE Program for Public Sector with at least 15 RFP per year | Limited institutional capacity to undertake EE promotion Program | Institutional Framework for EE promotion for approval by the end of Yr 2 | Official govt. publications Progress Reports | The institutional framework for EE responds to local economic, social and cultural specificities |
| Output 2.2: EE Projects realized under the ESCO approach by the Government increased ;(Public building owners/ operators have been exposed to PBI program to access EE services and applied its recommendations) | Number of ESCOs and building owners/ operators trained on the PBI program (at least 400 persons) Use of the PBI approach for RFP process in public buildings | No tender process for public building under performance contract | 15 RFP a year based on the PBI concept (on average) | Bi annual report Mid-term evaluation reports Progress Reports | Enabling EE promotion regulation adopted by the Government to make possible the PBEETB concept |
| Output 2.3: Capacity building (CB) offered to Public Building Owners/ Operators and ESCOs in developing and implementing selected projects on a pilot basis for public sector buildings | CB provided to public building organizations is effective for a demonstration of EE project implementation Number of ESCOs provided with technical assistance to develop public EE projects At least 80% of satisfaction expressed by public building organizations on TA | Limited CB possibilities in EE sector to public building operators/owners Limited experiences in EE in public building projects Limited experience in ESCO projects in public buildings | 5 pilot projects for public building sector by the end of Yr 3 At least 30 ESCOs provided with technical assistance to develop public EE projects | Bi annual report Official govt. publications Mid-term report | Public Sector EE reform adopted by the Government to enable ESCO projects |
| Outcome 3: Interest enhanced in the replacement of energy-inefficient CFC-using chillers | Design the full program complying with the Montreal Protocol regarding CFC-based equipment removal | The inventory of CFC-based chillers is accepted as 1,000 centrifugal chillers | Up to 40 CFC-based chillers replacement demonstration projects using MLF co-financing implemented by the end of Yr 2 Effective promotional program for the replacement of CFC chillers | Bi annual reports Mid term report Technical Publication | Project design responds to Montreal Protocol requirement and local specificities |
| Output 3.1: Technical assistance (TA) provided to professionals on EE improvement combined with HVAC equipment replacement | Number of professionals trained on replacement of inefficient chillers (CFC and non-CFC) | None | 120 Professionals (ESCOs and Entrepreneurs) in the specific field of chiller replacement (non-CFC and CFC-based chillers). | M&E reports Progress Reports Mid term report | Professionals cooperate with the Project Management Unit Data from monitoring program (see Output 3.3) confirms efficiency gains from demonstration projects |
| Output 3.2: Technical guides drafted for professionals | Number of professionals using practical guides design to assist in CFC-based chillers replacement | None | At least 2 practical guides published on CFC-based chillers replacement 60 professionals using practical guides | Publication of practical guides | Guideline material developed by Yr 1 |
| Output 3.3: Pilot projects to evaluate the impact of the proposed CFC-based chillers replacement Program | Number of demonstration projects (40 CFC-based chillers replaced) Monitoring of energy consumption in sample buildings | None | Up to 40 proposed demonstration projects are field implemented to validate CFC-recovery and EE gains | Contracts with operators Monitoring reports | Availability of good testing sites (public buildings for pilot project) Data from monitoring of pilot projects are relevant |
| Outcome 4: EEGM made available to stimulate EE investment through ESCOs | The EEGM is operational Number of ESCOs and/or financial institutions using portfolio guarantees such as the EEGM | Few ESCOs can borrow from commercial Banks; they use ANEEL fund and own money or partly client money | At least 250 projects approved under the EEGM and provided with guarantees | Bi annual report Financial Audits Mid term report Final report | Willingness and interest from Financial Institutions to access the EEGM |
| Output 4.1: Local banks begin to treat energy savings as collateral in their lending evaluation matrix | Number of financial institutions which have defined target segments for EE financing and made relevant changes in internal procedures At least 2 employees in 10 FIs who know how to assess, structure and monitor loans/guarantee to EE transactions | A limited number of EE projects are implemented due to lack of financing, lack of ESCOs’ evaluated savings credibility | Drafting of new strategies for each participating FI in Years 1-2 in response to requests from ESCOs and other professionals New financial products available on the EE market by Yr 2 At least 5 financial institutions which have defined target segments for EE financing | Project Report FIs Publication Progress Reports M&E reports | Financing Professionals cooperate with the PMU to develop adequate products for the EE market Information from the ESCOs confirms cost effectiveness of EE measures resulting from demonstration projects |
| Output 4.2: The EEGM has been experimented and is fully operational | Number of projects approved under EEGM Amount of guarantees (PCGs) provided for qualified projects Number of ESCOs supported by EEGM | None | At least 250 projects approved under the EEGM and provided with guarantees | Project Report FIs Publication Progress Reports M&E reports | Energy Performance Contract (EPC) models comply with national business regulation |
| Outcome 5: Project monitoring and evaluation support | One progress report available per year M&E effective on time | None | 100% of planned Project monitoring and evaluation activities completed | Annual reports M&E reports | The PMU is established and fully operational |
| Outcome 6: Overall project management support | Project objectives and deliverables Alignment of sector policies with objectives of EE project | Minimal integration of EE issues in govt. building programs | Timely submission of all project reports Project objectives substantially met | Surveys of key stakeholders and donors Ministerial policy statements and annual programs | Willingness of key Authorities to become lead adopters of EE Improvement Program in Brazil |

- PROJECT BUDGET

- The proposed total GEF grant requested for project implementation is USD13.5 million. The details of the budget are elaborated upon in Table 12 below. UNDP, drawing upon funds approved under the Multilateral Fund (MLF) for the Implementation of the Montreal Protocol, will contribute USD 1.00 million in response to project Outcome 3, and participating private sector entities, including local banks and other private sector actors, will contribute through EE investments in the order of USD 93.22 million, and the IDB will contribute to the EEGM with USD15 million.  The Government, will provide USD 0.90 million for project management (in-kind contribution). The total co-financing input of USD 122.774 million.

Table 12	Financing structure of the project

Totals per donor:

- Additional information

- Co-financing letters and letters of endorsement

The below co-financing and endorsement letters have been attached as a separate document;

| Multilateral Fund of the Montreal Protocol | November 2005 |
| --- | --- |
| BNDES (Brazil National Development Bank) | 23 March 2006 |
| AES Eletropaulo | 23 March 2006 |
| Harmonia | 17 March 2006 |
| Banco Itaúu | 22 March 2006 |
| Eletrobrás | 17 March 2006 |
| ABESCO | 24 March 2006 |

- Stakeholder involvement plan

| Institution | Official Mandate | Role in project |
| --- | --- | --- |
| Government |
| Ministério do Meio Ambiente (Ministry of Environment) (MMA) |  | Leading Executing Agency in partnership with MMA Leading Agency of the NPSC Also Executing Agency of the Chiller Demonstration Project funded by MLF, so responsible for project linkages. Active leader in the implementation of the demonstration component for replacement of CFC chillers. Sub-partners include IUM and PROZON (outcome 3) Co-financing in kind with activities in the CFC sector Support / potential co-sponsorship to training activities Active Member in the PBI (outcome 2) Project website to be co-hosted by MME and MME |
| Ministerio de Minas e Energia - Ministry of Mines and Energy- (MME) |  | Partner to MMA for operational purposes and linkages purposes for the project. Responsible for linkages with PROCEL activities Member of the NPSC Co-financing in kind for activities in the EE sector for building. Support / potential co-sponsorship to training activities Leader Member in the PBI (outcome 2). Project website to be co-hosted by MME and MMA |
| BNDES (Development Bank of Brazil) | BNDES is a federal public company that is associated to the Ministry of Development, Industry and Foreign Trade, which has as an objective to long term financing of endeavors that contribute towards the development of the country. | Financing (providing credit risk only) to clients directly or via commercial banks and complementing the EEGM program. Special funds catering to EE including: FINAME – Machinery and Equipment Purchasing, Financing the ESCO Customers, PMAT – Public Lighting, Public Buildings Equity, and RELUX for Municipalities. Funding PROESCO, a special specific fund designed to meet the specific credit risk protection catering to the specificities of ESCOs. |
| ANEEL, Brazilian Electricity Regulatory Agency | Aneel's Mission - To provide favorable conditions for the electricity market to develop in a balanced environment amongst agents, for the benefit of society. Mandates electric energy distribution companies to invest in research and development (R&D), and in energy efficiency programs | Co-financing via the mandated EE program. Supports the project |
| International Organizations |
| UNDP-Brazil | Provision of TA grants for GOB’s various energy and environmental projects | GEF Implementing Agency; |
| Inter-American Development Bank | Provision of loans and TA grants for the Government’s various energy and Environment projects | Co-implementing Agency in charge of the oversight of the EEGM (Outcome 4) as described in the different sections of the project documents. |
| USAID (The United States Agency for International Development), | Technical and grants assistance to developing countries from the Government of USA including various environmental and electrification | Potential collaboration in first two years if willing to refocus on public building. Energy Program after 2007 is not yet secured. Potential adviser to PBI because of previous work |
| The World Bank | Provision of loans and TA grants for the Government’s various energy and environment projects | Linkage with the activities of the 3 country energy efficiency initiatives (India, China, Brazil) Potential linkage activities in the energy and environment sector |
| IFC | Provision of loan to provide sector for various energy and environment projects or equity in ESCOs | Potential linkage activities in the energy and environment sector. |
| Private Sector |
| AES-ESCO, ESCO Light, Efficienca, etc Harmonia, private insurance companies | Private sector utility linked ESCOs, with an interest on the growing market, including co-financing from their ANEEL obligations | Participation as active implementers Co-financing by access fund contribution from the ANEEL obligation especially for public and social sector Support / participation in the EEGM |
| ITAU, Banco Real, etc. | Banks with a particular known interest in the EE sector | Funding of ESCOs |
| Academic and Professional Associations |
| ABESCO (Associação Brasileira das Empresas de Serviços de Conservacao de Energia) Association of Brazilian Energy Service Companies | ABESCO's mission includes the promotion of the energy efficiency industry in Brazil and the competitive improvement of Brazilian companies through the sustainable development. | Advising member of the BPBEEI Potential co-organizer of training / marketing activities focused on ESCOs. Beneficiary of training / marketing activities |
| ABRAVA (Associacio Brasileira de refirgeracos, ar condicionado, ventilacao e aquecimento) | The association of HVAC manufacturers and installers. | Collaboration with ESCOs for implementation of projects (in operation and potentially in marketing, access to clients) Linkage on proper disposal / reclaiming of used CFC Linkage on training on HVAC (trainers and trainee) |
| Federaçao Brasileira dos Bancos (FEBRABAN) |  | Potential trainee/ partner, and linkage to banks for financing of EE programs |

- Operational rules of the EEGM

|  | ENERGY EFFICIENCY GUARANTEE MECHANISM (“EEGM”) SUBJECT TO CREDIT APPROVAL AND APPROVAL BY THE IDB’S BOARD OF EXECUTIVE DIRECTORS. |
| --- | --- |
| EEGM Structure | The GEF will deposit up to USD10 million with IDB. This deposit will act as first loss cash collateral for the issuance by IDB of Partial Credit Guarantees (“PCG”) with a maximum amount outstanding under the EEGM at the time of any PCG issuance, of USD25 million, and a maximum net exposure of the IDB of USD15 million at the time of nay OCG issuance. The EEGM will be managed by the third party Administrator who will request the IDB to issue PCGS for projects fulfilling the Eligibility Criteria. Part of the GEF deposit may be used to fund the costs of the Administrator and other operational costs of the EEGM. IDB will act as Guarantor of Record against the pledged GEF deposit. GEF will take first losses on the aggregate portfolio, not pro rata per PCG. |
| Availability and Tenor | PCGs will be issued during an availability period of 5 years and each PCG will have a maximum maturity of 7 years (i.e. maximum 12 year tenor for the EEGM). |
| Eligibility Criteria | EE projects in Brazil undertaken by ESCOs which are majority owned by entities of IDB Member Countries, excluding any projects with project parties active in sectors on the IDB’s Exclusion List. Other criteria would be proven technologies, certain types of EE Contract, and maximum and minimum project sizes (the average EE project size - i.e. the total energy savings -is expected to be in the region of USD500,000). Projects must also comply with the IDB’s integrity and Environmental and Social Requirements which would follow the requirements typical for FIs and be administered by the Administrator. |
| Partial Credit Guarantees (PCG) | The PCGs will fall into two categories: Performance Guarantees; Comprehensive Risk Guarantees. The PCGs may be issued either as co-financing guarantees alongside BNDES’ PROESCO program, under which BNDES funds 100% of commercial bank loans to ESCOs but assumes up to 80% of the repayment risk. The co-financing guarantee would cover up to 20% of the bank loan. BNDES has invited IDB to share up to 20% of the risk of PROESCO projects. The PCGs may also be used to guarantee bank loans outside of PROESCO. |
| Risks Guaranteed | The PCGs will cover the following risks using a standard PCG form: a) Performance Guarantees: shortfalls in realized energy savings amounts due by Clients under EE Contracts due to technical non-performance; payment default by the Client due to credit reasons will be excluded. b) Comprehensive Risk Guarantees: payment default under a loan or discounting facility for any reason. |
| Beneficiaries of the PCGs | Clients or commercial banks. Commercial banks. |
| Reimbursement | ESCOs will sign a Reimbursement Agreement with the IDB under which they will be liable to reimburse the IDB for any disbursements under a PCG. |
| Exposure Limits | IDB exposure will not exceed 50% of the projected energy savings of the EE project (per IDB policy the Bank may participate up to 50% of a financing program). Maximum exposure of the IDB at the time of PCG issuance, net of the GEF deposit, not to exceed USD15 million. There will also be portfolio limits to limit exposure to any one ESCO. |
| EEGM Administrator | An Administrator will be selected by the IDB under a tender process. The Administrator will originate, evaluate and structure the PCGs according to the Eligibility Criteria and will request the IDB to issue PCGs under the EEGM using an information form to be determined. The Administrator will monitor the exposure of the portfolio, providing current and projected default rates to the IDB each time a request is submitted, and will pursue recovery of any PCGs disbursed. The Administrator will be remunerated by a combination of upfront fees and part of the annual PCG premiums. Other operational costs of the Administrator may be funded out of the capital and/or interest on the GEF deposit. |
| Currency | The PCG will be denominated, and if called, disbursed to the Beneficiary in Brazilian Reais, subject to the Maximum Aggregate PCG Amount outstanding at the time of issuance of a new PCG. Premiums and fees will be paid in Brazilian Reais. The total amount outstanding under the EEGM may be above USD25 million in the case of currency appreciation. |
| Governing Law | PCG and Reimbursement Agreement under Brazilian Law if possible (subject to approval by IDB’s Legal Department). |
| Pricing | Each type of PCG will have different pricing based on projected default rates for the risks being guaranteed. The IDB will receive a market return for the risk underwritten based on default rates and other market benchmarks, and taking into account the first loss protection afforded by the GEF deposit. |
| EEGM approval process | Given the small average size of EE projects, the most efficient approval structure prior to the issuance of PCGs by the IDB will be based on project sizes. For guarantees below USD100,000, the IDB will issue the PCG within a five day period after receipt of confirmation by the Administrator of compliance with the Eligibility Criteria, credit guidelines and information requirements. For guarantees between USD100,000 and USD350,000, the IDB will issue the PCGs within a 15-day period on a non-objection basis. Guarantees above USD350,000 would require the IDB’s specific approval within a 20-day period. The IDB may decline to issue PCGs following receipt of the application from the Administrator. |

- EEGM guarantee exposure and investment leveraging

A financial model has been developed to forecast the performance of the EEGM. The financial model calculates the leverage that the GEF deposit generates, in terms of the number of projects that can be catalyzed by the EEGM and the corresponding US Dollar value of EE energy savings generated. The financial model was used to develop a Base Case, to demonstrate a likely scenario for the evolution of the EEGM.   The drivers of the financial model are given in table 13 below. In the model, the term “project size” corresponds to the total energy savings generated by the EE project.  It has been assumed that the EEGM will be most used evenly for co-financings alongside PROESCO, non-PROESCO performance guarantees and comprehensive guarantees. To be conservative, a slow ramp up was assumed for PROESCO co-financings, with the non-PROESCO interventions growing initially at a faster rate in the absence of a fully operational PROESCO.

Table 13 	EEGM Base Case – Key Drivers

Using these assumptions, Table 14 below illustrates the gradual ramp up of exposure under the EEGM and its subsequent reduction as the guaranteed loans are amortized, for each type of guarantee and on a consolidated basis. Under the Base Case, approximately 250 guarantees are issued over the 5-year availability period, the bulk of which would be originated by BNDES under PROESCO, given that PROESCO is the most competitive instrument available to finance EE projects in Brazil due to its low interest rate. In total, USD35 million of EE project risks would be guaranteed, leveraging almost USD 125 million in energy savings, meaning that USD 90 million in energy savings will have been co-financed by other entities, such as BNDES and commercial banks. The USD 125 million in energy savings is equivalent to a leverage factor of the GEF deposit of 10:125.  Using the assumed Base Case default rates, USD2.8 million in guarantees (or 7.8% of total guarantee amounts) would be written off over the life of the EEGM and absorbed by the GEF deposit.

Table 14 	EEGM Base Case forecast

- Terms of reference of key project staff

DRAFT

Project Director

TITLE				: Project Director

ORGANIZATION		: Ministry of Environment

REPORTS TO			: National Project Steering Committee (NPSC)

DURATION			: Approximately 200 weeks during 7 years

REMUNERATION		: Commensurate with qualifications, skills and experience

RESPONSIBILITIES & DUTIES

- Coordinate the management and implementation of activities as set out in the Project Document (except for Outcome 4 as per specificities of EEGM administration);

- Provide support and assistance to the National Project Steering Committee

- Provide overall guidance to the Project Manager and the Project Management Unit (PMU) for project execution and assist the PMU and consultants in carrying out their assignments

- Act as intermediary between the PMU and Government of Brazil and coordinates with the ministries involved

- Review and approve ToRs, including consultants and contracted parties

- Review consultants’ reports, project budget revisions and all other administrative arrangements as per ministerial and UNDP procedures

- Provide technical assistance in energy efficiency policy discussions and development;

- Advise on in overall project monitoring and evaluation; and

- Undertake other management duties that contribute to the effective functioning of the project.

REQUIREMENTS

- Senior level official within Ministry of Environment

- At least 15 years of experience in operation and management of energy efficiency programmes and projects in Brazil

Project Technical Manager

TITLE				: Project Technical Manager

ORGANIZATION		: UNDP

REPORTS TO			: UNDP, Ministry of Environment and NPSC

DURATION			: 336 weeks during 7 years (one-year renewable)

REMUNERATION		: Commensurate with qualifications, skills and experience

REQUIREMENTS

Applicants must have post-graduate (at least Master’s) training in any one of the following fields of study:

- Development economics with a strong energy systems planning and management component; and/or engineering with energy systems planning focus and/or economics background.

- Work experience with energy efficient technologies, in particular in buildings

- At least ten years experience in the area of energy efficiency;

- At least seven years work experience at senior management level with demonstrable program or project level management skills and ability to coordinate activities involving a large contingent of professional consultants drawn around the country and/or internationally;

RESPONSIBILITIES

Directing technical activities of the Project:

- Follow up of project management and co-ordination with the Project National Coordinator;

- Forward planning;

- Liaising with project participants and stakeholders;

- Preparation and presentation of project status reports to the Project Steering Committee;

- Preparing consultants and subcontractors terms of reference;

- Technical supervision of contracts;

- Technical assistance; and

- Project execution of all technical tasks identified under the project specified in the Project Document.

DUTIES

- Liaise with National Coordinator on the day-to-day management of the PMU, specially on issues of technical expertise, and actual project implementation and reporting;

- Lead the development of detailed project design including preparation of subcontractors terms of reference, identification and selection of national, regional and international subcontractors, cost estimation, time scheduling, contracting, and reporting on forward planning of project activities and budget;

- Coordinate activities of consultants and subcontractors including contract management, direction and supervision of  field operations, logistical support, review of technical outputs/reports, measurement /assessment of project achievements and cost control;

- Supervise the selection of the sites, profiling, feasibility analysis and actual installation and follow-up evaluation of energy efficient options in buildings;

- Assist in the design, supervision and where possible delivery of the training and outreach activities of the project and take a lead role in the organization of project workshops and dissemination of results of the projects;

- Plan and coordinate various workshops identified in this Project Document;

- Work closely together with the National Project Steering Committee (PSC) and UNDP as well as the Brazilian counterparts (ministries, banks, ESCOs, clients);

- Allocation of the contribution of GEF and other co-financiers according to the annual work plans and financial reports

- Preparation of annual work plans, quarterly financial and progress reports and the annual APR (annual project implementation review report);

- Inform NPSC and UNDP on project progress and budget variations and advising on the policy direction at PSC meetings;

- Maintain records/minutes of proceedings of the NPSC;

- Take responsibility for the quality and timing of project outputs;

- Assist in overall project monitoring and evaluation; and

- Undertake other management duties that contribute to the effective functioning of the project.

DELIVERABLES

- Finalized Terms of Reference for consultants and subcontracting

- Quarterly work plan and financial reports

- Annual progress reports

- Minutes of PSC meetings

- Agenda for project workshops and meetings

Country: BRAZIL

UNDAF Outcome(s)/Indicator(s):

Outcome 5. More efficient use of available resources is ensured to promote an equitable and environmentally sustainable economic development

Expected Outcome(s)/Indicator (s):

5.2 Public policies with increased mainstreaming and crosscutting of the environmental dimension in their design, implementation and management.

Expected Output(s)/Indicator(s):

MYFF Service line 3.3. – Access to sustainable energy services.

Implementing partner:						Ministry of Environment

(designated institution/Executing agency)

Other Partners:							Inter-American Development Bank

# Footnotes

The Hydroelectric Power Option In Brazil Environmental, Technological And Economic Aspects, Ventura Filho, Altino Itaipu Binacional Foz Do Iguaçu, Brazil., World Energy Council, http://www.worldenergy.org/wec-geis/publications/default/tech_papers/17th_congress

The Hydroelectric Power Option In Brazil Environmental, Technological And Economic Aspects, Ventura Filho, Altino Itaipu Binacional Foz Do Iguaçu, Brazil.

See section on barriers to EE in Brazil

Geller, H.S. (1994) O uso eficiente da electricidade: uma estrategia de desenvolvimento para o Brasil. Rio de Janeiro: INEE.

Information drawn from: CORE International Moving Markets for Energy Efficiency in Brazil, 1999.

The global electricity market was 387 TWh in 2007, of which 44% was used in buildings (industrial, commercial, residential and public facilities). With an average cost of USD 0.14/kWh and conservative estimate of the savings potential of 20%, the Brazilian EE market in buildings could represent approximately USD 4.77/year

Key base interest rates have been reduced by 1.5% p.a. by the Central Bank of Brazil on March 12, 2009, to 11.5% p.a

Only approximately five large ESCOs have a gross income above US$1 million per year.

Banco Nacional de Desenvolvimento Econômico e Social

To date, Banco Itaú, BGMG, Banco do Brasil, Bradesco and CEF

In addition, interest was diminished when the original risk coverage of 90%  of loans, was reduced to the current 80%; ESCOs raise concerns as to whether banks would be able to finance the remaining 20%.

BNDES Energy Division normally works on large energy production projects. EE projects with low budget are put at the end of the pipeline. More (EE) experts cannot be hired,  due to current BNDES corporate policy constraining the hiring of new staff, while its confidentiality regulations do not allow hiring of external consultants.

Major utilities are LIGHT, AMPLA, ELETROPAULO, CPFL, ELEKTRO, CEMIG, COPEL, COELBA, CELPE, AES SUL and CEB

For the purposes of the project, the public sector encompasses federal, state and municipal administrations, as well as public service providers, such as schools and hospitals.

There are around 5,000 federal public buildings and more than 10,000 state public buildings. The training should be distributed around the country in at least 2 cities of each geographical region, so for each course it should be repeated 10 times

despite the fact that Brazilian stakeholders consulted all agreed that, on average, chilling represents 70% of electricity consumption in buildings

www.ipmvp.org

Any project that has the potential to generate EE benefits in buildings would be eligible to access EEGM support, assuming that required financial and technical criteria could be met. As a result, EE projects that target lighting, electricity distribution (transformer, power factor), HVAC (including ventilation, air conditioning, heat exchangers, heat control systems, pumping, steam distribution, boilers, chillers, etc), as well as self-power production, could be eligible. To be as cost-effective as possible, it is likely that ESCOs would bundle many of alternative technologies/processes in there projects.

Out of the total US $13.5 million being requested for this FSP to help remove policy, capacity, finance and technology barriers that stand in the way of widespread adoption of EE measures and technologies in buildings in Brazil. The GEF grant is expected to be held as a deposit by a trustee bank in New York as collateral for the issuance of the guarantees by the IDB.

The IDB may consider increasing its relative contribution to similar guarantee schemes  to be developed in other IDB Member Countries as the EEGM may be replicated based upon a the proven track record of success in Brazil under this component of the project.

BNDES has worked with FDIC structures previously, including a carbon credit fund

In other guarantee programs, the IDB receives a percentage of the risk premium charged by the beneficiary bank on the residual unguaranteed portion, payable on the amount guaranteed.

See description under ‘Outcome 4’

National Institute of Metrology, Normalization and Industrial Quality - INMETRO

The ‘end-of-project impact’ study will include estimation of the direct emissions, based on the audits and investment plans and on a measurements in a sample of energy efficiency in buildings (where these have been implemented or an investment decision has been made)

Part 4 in Section D calculates that about 250 could be covered.

3.717 million MWh = 250 * 20 * 0.125 * 100,000/1000

These are possible roles. Final designations will be determined during the project inception.

# Text boxes

Brazil

Figure 1	typical EE project financing structure using shared savings contract as collateral

Total Budget:		$ 136,274,000 USD

Allocated resources:	3,305,000 GEF

- Government		414,000 (in-kind)

- Other:

  - Banks, ESCOs, end-users				106,360,000

  - MLF	1,000,000

  - GEF IDB	10,195,000

  - IDB	15,000,000

Programme Period: 2009-2013

Programme Component: Energy and Environment

Project Title: Brazil: Market Transformation for Energy Efficiency in Buildings

Award ID: 00048524

Project Duration:	7 years

(September 2009/August 2016)

Management Arrangement: NEX

62000

GEF

UNDP

Management Unit

Project

UNDP

62000

GEF

evaluation

feedback and

learning, adapative

Monitoring,

62000

GEF

UNDP

Implementing Partner (Exec. Agency):

BRA10

Business Unit:

Ministry of Environment

using chillers

of inefficient CFC-

in the replacement

Interest enhanced

Outcome 3:

Initiative, PBI)

(Public Sector

sector buildings

financing for public

commercial

services and

Access to EE

Outcome 2:

and public sectors

building in private

through capacity

investments

Enhanced EE

Outcome 1:

62000

GEF

UNDP

62000

GEF

UNDP

Project ID:

Award Title:

Project Title:

Market Transformation for Energy Efficiency in Buildings

PIMS 3665 CC FSP Energy Efficiency in Buildings

00058719

00048524

Award ID:

(through ESCOs)

investments

stimulate EE

made available to

: EEGM

Outcome 4

3,305,000

744,800

345,000

384,400

460,900

417,200

449,200

503,500

TOTAL

490,000

77,500

68,000

67,500

68,000

67,500

70,500

71,000

Sub-total

-

-

-

-

-

-

-

-

Miscellaneous

74500

30,000

12,000

2,000

2,000

2,000

2,000

5,000

5,000

Supplies

72500

40,000

5,500

6,000

5,500

6,000

5,500

5,500

6,000

Travel

71600

420,000

60,000

60,000

60,000

60,000

60,000

60,000

60,000

Contractual Services-Indv

71400

263,500

104,500

5,000

5,500

71,500

5,500

5,500

66,000

Sub-total

4,500

-

500

1,000

1,000

1,000

1,000

-

Miscellaneous

74500

30,767

8,267

4,500

4,500

4,500

4,500

4,500

-

Professional Services-audit

74100

35,000

7,000

-

-

14,000

-

-

14,000

Travel

71600

70,267

36,267

-

-

17,000

-

-

17,000

Local Consultants

71300

122,967

52,967

-

-

35,000

-

-

35,000

International Consultants

71200

-

-

-

-

-

-

-

-

Sub-total

-

-

-

-

-

-

-

-

IDB

-

sub-total

-

Miscellaneous

74500

-

Travel

71600

-

Local Consultants

71300

-

International Consultants

71200

1,183,330

328,630

112,700

142,000

136,900

151,700

157,700

153,700

sub-total

15,000

2,000

2,000

2,500

2,500

2,000

2,000

2,000

Miscellaneous

74500

37,000

5,500

5,500

5,500

5,500

5,000

5,000

5,000

Audio visual & Printing Prod.costs

74200

5,830

-

2,970

1,600

1,500

1,500

1,400

1,400

1,400

Rental and Main Equip

73400

7,000

-

1,400

1,600

1,500

1,400

1,300

1,300

1,300

Rental and Main Premises

73100

9,000

-

1,000

-

2,000

-

-

4,000

4,000

Info Tech Equipment

72800

7,000

-

7,000

-

5,000

2,000

-

2,000

5,000

Supplies

72500

197,000

-

8,000

20,000

35,000

35,000

40,000

40,000

35,000

Travel

71600

660,000

270,000

60,000

60,000

60,000

70,000

70,000

70,000

Local Consultants

71300

150,500

58,500

8,000

16,000

16,000

18,000

18,000

16,000

International Consultants

71200

95,000

13,000

14,000

13,000

13,000

14,000

14,000

14,000

Contractual Services-Co

74100

1,368,170

234,170

159,300

169,400

184,500

192,500

215,500

212,800

sub-total

13,200

2,000

1,800

1,800

1,900

1,800

1,900

2,000

Miscellaneous

74500

50,000

10,000

5,000

5,000

10,000

5,000

10,000

5,000

Audio visual & Printing Prod.costs

74200

11,300

5,900

900

900

900

900

900

900

Rental and Main Equip

73400

7,000

3,500

500

600

600

600

600

600

Rental and Main Premises

73100

9,000

5,000

-

-

-

2,000

-

2,000

Info Tech Equipment

72800

8,000

7,100

100

100

100

200

100

300

Supplies

72500

10,000

1,000

1,000

1,000

1,000

2,000

2,000

2,000

Equipment and furniture

72200

300,000

20,000

30,000

40,000

40,000

50,000

60,000

60,000

Travel

71600

590,000

130,000

75,000

75,000

75,000

75,000

80,000

80,000

Local Consultants

71300

131,250

31,250

15,000

15,000

15,000

15,000

20,000

20,000

International Consultants

71200

238,420

18,420

30,000

30,000

40,000

40,000

40,000

40,000

Contractual Services-Co

72100

Total (USD)

Year 7

Year 6

Year 5

Year 4

Year 3

Year 2

Year 1

Description/Input

ERP/ATLAS Budget

Code

Account

Budget

Atlas

name

/ donor

Fund ID

Agency)

(Impl.

Party

Resp.

Atlas Activity

GEF Outcome /